## Slide 1
NASA Jet Propulsion Laboratory
Using UAVSAR, AVIRIS, and AirSWOT to Model Coupled Water Flow and Sediment Transport for Delta Building within the Wax Lake Delta, Louisiana to Inform Coastal Restoration Efforts
Louisiana Ecological Forecasting II
From left to right: Mark Barker, Emily Beck, Erika Higa (Project Lead)
US Naval Research Laboratory, Dr. Richard Crout
Louisiana Universities Marine Consortium, Dr. Alex Kolker
Dr. Cathleen Jones, Science Advisor, NASA Jet Propulsion Laboratory
Dr. Marc Simard, Science Advisor, NASA Jet Propulsion Laboratory
Doug Edmonds, Delft3D
John Barras, USGS
Dr. John Shaw, University of Arkansas
Brittany Zajic and Raul Garcia, NASA DEVELOP
Eight generalized land cover types were derived from AVIRIS-NG data, six land cover types were derived from Landsat 8 OLI data, and more work needs to be done to include vegetation biomass and roughness in Delft3D.
The modeled result will need further calibration with AirSWOT and in situ water level data to accurately model the aggregation process at Wax Lake Delta.
A combination of earth observation data and in situ data can be used to model the water flow in the delta with Delft3D.
Erosion, land subsidence, and sea level rise along the Louisiana coast have led to 4900 km2 of land loss since the 1930's. It is estimated that Louisiana has the potential to lose an additional 4500 km2 over the next 50 years if no restoration action is taken. While most of the Louisiana coast is eroding, the Wax Lake Delta has continued to grow at a rate of approximately 5 km2 per year since the 1970's. Currently, labor intensive boat-based surveys are conducted to understand the delta building dynamics at Wax Lake. There have been a number of studies on the natural processes that contribute to this growth, but many of these studies lack tested models. We used remotely-sensed and in situ data, as well as Deltares Delft3D modeling software, to model water flow and sediment transport in the delta—calibrating the model using AirSWOT data. Model outputs will be used to inform coastal research by project partners at the United States Naval Research Laboratory in Mississippi and the Louisiana Universities Marine Consortium to assist the efforts of coastal managers in predicting coastline change and planning restoration projects to reduce land loss along Louisiana's coast.
Extrapolate delta vegetation elevations using UAVSAR
Model water flow and sediment transport using Deltares Delft3D
Calibrate resulting model with AirSWOT
Examine delta formation processes to gain a better understanding of why the Wax Lake Delta is aggregating
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Erika Higa (Project Lead), Emily Beck, Mark Barker
DEVELOP National Program at NASA Jet Propulsion Laboratory
UAVSAR
Modeled Water Flow
In Situ Data: Vegetation Species, Water Level, Flow Rate
Delft3D Hydrological Model
Vegetation Elevation Mask from UAVSAR
(Python)
Modeled Sediment Transport
Calibrate Model using AirSWOT Data
Raster Datasets of Bathymetry
(ESRI ArcGIS)
Study Period: April 2015 – May 2015
Wax Lake Delta, Louisiana
AirSWOT
AVIRIS-NG
Landsat 8 OLI data classified into six generalized vegetation classes
Bathymetry layer that was created from the classified UAVSAR image merged with multiple topo-bathymetric datasets
Vegetation Species Classification from AVIRIS
(Exelis ENVI)
ISODATA Unsupervised Vegetation Classification of AVIRIS-NG data with clouds masked
Left: Modeled water level in meters during one time step from the preliminary Delft3D model of the Wax Lake Delta
Right: Map of AirSWOT swath and CRMS stations
+
Landsat 8 OLI