## Slide 1: Colorado Water Resources
Utilizing NASA Earth Observations to Identify Water Quality Sampling Sites in Denver, Colorado
Geordi Alm (Project Lead)
Janice Maldonado Jaime
Rachel Wolf
Amanda Collins

## Slide 2: Water Resources
Globally, less than 0.01% of surface water is stored in freshwater lakes, streams, and rivers.
  Primary source:
    Runoff produced by snowmelt
Photo by Jimmy Thomas CC BY 2.0
Notes: Water is an important and necessary n
The primary source of freshwater in some mountainous and arid regions is runoff produced by snowmelt, as in the state of Colorado. Seasonal snowmelt from these mountains provides the water that eventually makes its way into the Denver Water Collection System. Situated in the eastern part of the Front Range of the Rocky Mountains, and in the South Platte River Valley, the city of Denver receives a mean annual snowfall and precipitation of 147.32 cm and 38.07 cm, respectively (NWS-WFO Denver-Boulder, 2015). Denver Water uses five mountain reservoirs to collect surface water from streams, rivers, and lakes over a watershed of 8,000 km2 (Denver Water, 2014). Historically, these reservoirs have provided over 1.3 million people with clean water; in 2014, Denver Water reported that several contaminants from sources such as mine sites, agriculture, and oil wells, had been detected in the water supply (Denver Water, 2014).
atural resource essential to the survival and health of ecosystems and all forms of life.

## Slide 3: Denver Water Collection System
Insert Picture
  Suggestions: Basemap of Denver, DW collection map, some reservoir, faucet running water…
Denver Climatology:
  Mean Annual Snowfall 147.32 cm
  Mean Annual Precipitation 38.07 cm
Five mountain reservoirs collect surface water over a watershed of 8,000 km2
Provides clean water for over 1.3 million people
Several contaminants had been detected in the water supply

## Slide 4: Major Wildfires
Destructive fires can affect watersheds and largely reduce vegetative land cover.
Colorado’s semi-arid climate natural re-growth takes several years.
Loss of Vegetation Exposure of Soil
Increase Water Runoff
Photo by David Stein CC BY 2.0
Photo by USDA CC BY 2.0
Notes: Fires result in loss of vegetation exposure of soil to erosion and increased water runoff that may lead to flooding increased sediment debris flows and damage to critical natural and cultural resources.
Forest fires, depending on the severity, can have a massive impact on an area’s watershed. A destructive fire will largely reduce vegetative cover which leaves the soil vulnerable to raindrop impact and reduces rainfall infiltration and storage, thus allowing erosive overland flow to occur more easily (Elliot and Vose, 2006). As a result, more sediment is washed into the water and water temperatures rise. The sediment often contains organic carbon, which contaminates the water supply; the increased water temperature changes the ecology of the water system, including the rate that contaminants are cycled through the ecosystem (UMCES, 2010). Vegetative re-growth can reverse the damage to the soil caused by fire, but in Colorado’s semi-arid climate natural re-growth takes several years (Nijhuis, 2012). If a major rainstorm or flood occurs before the area is able to re-grow its vegetation, all the loose sediments will be carried into the nearby creeks, streams, and rivers. These sediments often contain contaminants such as uranium and nitrate, which stem from the erosion of natural deposits, and organic carbon, which is often added into the water system by agriculture and urban runoff (Allain and Jones, 2013; Denver Water, 2014). Organic carbon is a major contributing factor for the decline in water quality, for it readily reacts to the chlorine used to treat water. The reaction forms trihalomethanes and haloacetic acids, which at elevated levels increase chances of cancer and birth defects (New Hampshire Department of Environmental Services, 2006; Allain and Jones, 2013; EPA, 2013). The amount of organic carbon that enters the water system is determined mostly by the type of soil it is in. Different soils will dispel the carbon at different rates; those with greater organic content dispel carbon more quickly, causing the water system to have increased amounts of organic carbon (Allain and Jones, 2013).

## Slide 5: Major Wildfires
Wildfires produce organic carbon, which contaminates the water supply
  Contributing factor for the decline in water quality
Photo by Soil Science CC BY 2.0
Photo by USDA CC BY 2.0

## Slide 6: Community Concerns
Source Contaminants
Wildfires: Organic Carbon
Mine: Uranium
Agriculture: Pesticides, Nitrates
Wildfires: Organic Carbon
Mine: Uranium
Agriculture: Nitrate and Pesticides
Photo by Slworking2 CC BY 2.0
Photo by Al_HikesAZ CC BY 2.0
Photo by Global Water Partnership CC BY 2.0

## Slide 7: Project Partners
  Denver Water
  Diego Portillo ● Linda Rosales ● Sheila Pelczarksi
Photo by elPadawan CC BY 2.0

## Slide 8: Study Area
Study Period
  May 1994 – June 2013

## Slide 9: Objectives
Utilize land cover data to identify existing infrastructure and possible pollution sources in the Denver Water Collection System
Assess the placement of current water sampling sites
Create a map identifying optimal sampling sites
Photo by elPadawan CC BY 2.0
Notes: Utilize land cover data from Denver and surrounding areas to identify existing infrastructure and possible pollution sources in the Denver Water collection system
Assess the placement of current water sampling sites
Create a map identifying optimal sampling sites

## Slide 10: NASA Earth Observations
Landsat 7
Landsat 7
Landsat 7
Sensor: Enhanced Thematic Mapper +
(ETM +)
Used for Land Cover
Landsat 7
National Land Cover Database (2011)
Cropland Data Layers

## Slide 11: Methodology
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data
Acquisition
Data
Processing
Data
Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Notes: NASA Earth observations
  Landsat 7 ETM+
  Landsat 8 OLI/TIRS
Acquisition & Processing
  Denver Water provided us with the current water sampling sites and the areas of the fires
  The National Hydrological Dataset (NHD) provided watersheds, rivers, streams, and water bodies
  Crop, soil type, and land data was obtained from ___
  Using the RUSLE model, a pollution risk assessment map was created
  [other types of processing things we’re going to do]
Analysis

## Slide 12: Methodology
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data
Acquisition
Data
Processing
Data
Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Notes: NASA Earth observations
  Landsat 7 ETM+
  Landsat 8 OLI/TIRS
Acquisition & Processing
  Denver Water provided us with the current water sampling sites and the areas of the fires
  The National Hydrological Dataset (NHD) provided watersheds, rivers, streams, and water bodies
  Crop, soil type, and land data was obtained from ___
  Using the RUSLE model, a pollution risk assessment map was created
  [other types of processing things we’re going to do]
Analysis

## Slide 13: Methodology
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data Acquisition
Data Processing
Data Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Data
Acquisition
Data
Processing
Data
Analysis
Land Cover
Landsat 7 ETM+
National Land Cover Database (2011)
Cropland Data Layer
Land Cover Classes and Crop Types Identification
Point Source Contaminant Assessment
Revised Universal Soil Loss Equation (RUSLE)
Water Sampling Sites
Denver Water
Mapping potential areas for water sampling sites
Soil Types
USDA
Wildfires
Denver Water
Risk Areas Classification and Validation
Notes: NASA Earth observations
  Landsat 7 ETM+
  Landsat 8 OLI/TIRS
Acquisition & Processing
  Denver Water provided us with the current water sampling sites and the areas of the fires
  The National Hydrological Dataset (NHD) provided watersheds, rivers, streams, and water bodies
  Crop, soil type, and land data was obtained from ___
  Using the RUSLE model, a pollution risk assessment map was created
  [other types of processing things we’re going to do]
Analysis

## Slide 14: Results
Final Maps
Discussion
Validation:
  Uncertainty/Error Analysis

## Slide 15: Conclusions

## Slide 16: Benefits to End Users
Improve efficiency of water monitoring system.
Support Denver Water’s mission to provide high-quality water to Denver and its surrounding suburbs using a resilient and reliable system.
Photo by Tobias CC BY 2.0
Photo by Matt Santomarco CC BY 2.0

## Slide 17: Limitations

## Slide 18: Future Work
Assess placement of water sampling sites after the Front Range and Eastern Colorado Floods
    September 2013
Photo by littlegreenfroggy CC BY 2.0

## Slide 19: Acknowledgements
Dr. Kenton Ross
NASA DEVELOP National Program- Science Advisor
Diego Portillo
Denver Water
Linda Rosales
Denver Water
Sheila Pelczarksi
Denver Water
Nathan Owen
NASA DEVELOP - Langley Center Lead
This material is based upon work supported by NASA through contract NNL11AA00B and cooperative agreement NNX14AB60A.