## Slide 1
Utilizing NASA Earth Observations to
Identify Harmful Algal Blooms in the Chesapeake Bay
Tyler Rhodes
Jessica Jozwik
Jakub Blach
Zachary Tate
Arika Egan (Project Lead)
Virginia Water Resources II

## Slide 2
Study Area
Study Area:
Lower Chesapeake Bay
Study Period: August 17th, 2015
Notes: Our Study Area is comprised of Virginia’s Lower Chesapeake Bay, The James River, The York River, The Elizabeth River, and Mobjack Bay.
We used observational and in-situ data from August 17th, 2015

## Slide 3
Image Credit: Wolfgang Vogelbein, York River, 8-17-2015
Harmful Algal Blooms (HABs)
Population Growth
Nutrient Runoff
Excessive Growth of Algae
Notes: The population of the Chesapeake Bay now pushes 18 million people.
Increasing population has lead to an increase in nutrient runoff into the Bay. Agricultural and urban runoff, vehicle emissions, sewage treatment plants, and the burning of fossil fuels all are responsible for nutrient loading in the Chesapeake Bay.
Increased nutrients promote excessive growth of algae.
Image source: Directly provided by VIMS

## Slide 4
Degrade water quality
Reduce Sunlight
Deplete oxygen
Produce toxins
Threaten
Fishing industry
Tourism industry
Ecological health
Human health
Community Concerns
Jennifer Graham. Harmful Algal Blooms. 10/19/2015
Mike Hooper. Dead Fish Washed Ashore during Golden Alga Toxic Bloom. 10/19/15
Notes: HABs block the penetration of sunlight through the water column, reducing the amount of available light for photosynthesis and plant growth.
As they die and decompose, they deplete dissolved oxygen in the water that is necessary to sustain animal life.
Certain species produce toxins that can mutate fish, cause human illness, and give off unpleasant smells.
As a result, the fishing industry is harmed, beaches are closed, human health is threatened, and areas of the Bay are less capable of sustaining plant and animal life.
Image credit: Provided directly from VIMS

## Slide 5
HAB task force
  Detect and study
HAB Hotline
  Report
VA Health Department
  Respond
Current Methods
Image Credit: Wolfgang Vogelbein, York River, 8-17-2015
Notes: There are two ways HABs are Detected: Through HAB Task Force Testing and Reports to the HAB Hotline
HAB TASK FORCE:
  Comprised of VIMS, DEQ, ODU, VA Dept of Health and VA Marine Resources Commission
  Responsible for Detecting and studying HABs.
    Maintains 20 fixed testing stations throughout the bay. Test water quality parameters and genetic testing of phytoplankton monthly from May-November
24 HOUR HAB HOTLINE
1. Relies on community members to report suspicious smells, colors, or fish kills.
There is currently no reliable method of real-time monitoring of HABs in the Chesapeake Bay. Researches must coordinate data collection cruises to gauge severity and duration of HABs, and must organize costly flyovers to study magnitude of the blooms. We thus seek to remedy this by…
Image Credit: Provided to us directly from VIMS

## Slide 6
routine and emergency assessment of HABs
Objectives
Create
a python tool that processes raw Landsat 8 OLI images and produces a chlorophyll-a map
Improve
Cultivate
a better understanding of the causes and impacts of HABs
Develop
an algorithm to combine Landsat 8, and in situ data to estimate chlorophyll-a concentrations
Notes: The goal of this project was to create a python tool to be used in ArcGIS that will produce a map of chlorophyll concentration for the Chesapeake Bay Watershed. It will do this by taking in Landsat 8 data and processing it with an algorithm created during this project.
By identifying the locations of HABs, our partners will be able to analyze the area to better understand the cause of the bloom.
New Landsat imagery of the watershed is produced every 16 days. The speed of this production, combined with the estimation tool, will allow our partners to more effectively monitor HABs when they occur. This is more efficient than the current system of routine monitoring and civilian reports of HABs.
This tool will better help determine the size, duration, frequency, and cause of HABs. These data are important factors in policy writing and can help improve regulations to prevent HABs.

## Slide 7
NASA Earth Observations
Landsat 8 OLI
Notes: Landsat 8 OLI: Downloaded with USGS Earth Explorer. Path 14 Row 34 and Path 15 Row 34 captured our study area. 30m resolution

## Slide 8
Create masks for land, clouds, shallow water and turbid water
Match Landsat and VIMS data
Combine layers into exported table
Landsat 8 OLI/TIRS reflectance bands
VECOS in situ water quality data
NOAA bathymetry data
Run linear and nonlinear regressions
Use best fit regression model as predictive model
Acquisition
ArcGIS
R
Methodology I

## Slide 9
Create masks for land, clouds, shallow water and turbid water
Match Landsat and VIMS data
Combine layers into exported table
Landsat 8 OLI/TIRS reflectance bands
VECOS in situ water quality data
NOAA bathymetry data
Run linear and nonlinear regressions
Use best fit regression model as predictive model
Acquisition
ArcGIS
R
Methodology I

## Slide 10
Masks
1
2
3
Land and cloud pixels are removed
Shallow (<2m) pixels are removed
High sediment concentrations are removed
Notes: We started with Raw Landsat data. The first image on the top left is Landsat 8 Band 1 from August 17th, 2015. Land pixels are removed by creating a water mask with the Normalized difference vegetation index. Clouds are removed using a cloud mask provided by EarthExplorer.
Next, using Bathymetry provided by NOAA, pixels corresponding to a depth of 2 meters or less are removed. The top middle image shows the bathymetry mask over the land and cloud removed image from the bottom left. The result is the bottom middle image.
Finally, high sediment concentrations are removed, using a model that calculated the Normalized Difference Turbidity Index. The top right image shows the sediment mask over the land, cloud, and shallow pixel removed image of the bottom middle. The final result is an image with land, clouds, shallow pixels, and high sediment concentrations removed, shown on the bottom right.
Image credit: NASA DEVELOP Wise County

## Slide 11
Create masks for land, clouds, shallow water and turbid water
Match Landsat and VIMS data
Combine layers into exported table
Landsat 8 OLI/TIRS reflectance bands
Aqua MODIS chlorophyll-a
VECOS in situ water quality data
NOAA bathymetry data
Run linear and nonlinear regressions
Use best fit regression model as predictive model
Acquisition
ArcGIS
R
Methodology I

## Slide 12
Initial Results
Notes: Notice the data flow trail in the image on the left. The image the dataflow is overlaid on is a color composite of Landsat bands 5, 4, and 3, a typical combination for highlighting chlorophyll. On the image, higher chlorophyll values are in red. The image has been slightly enhanced to show where a few data inconsistencies lie. The data does not match up in the image in several places, most obviously at the locations circled in purple. Even if the 543 composition doesn’t report accurate concentrations, the range of values should report where there is more and less chlorophyll. The Landsat range doesn’t match up with the VIMS range.
When plotting in R, the data was very inconsistent, with R squared values no greater than 0.2.
Image credit: NASA DEVELOP Wise County

## Slide 13
Initial Results
Formula | R2 | Adj R2 |  | formula | R2 | Adj R2
~exp(b1/b2) +b1+ b2+ b3+b4 | 0.1868 | 0.1855 |  | ~exp(b4/b3) +b1+ b2+ b3+b4 | 0.1889 | 0.1877
~exp(b1/b2) +b1+ b2+ b3+b5 | 0.1796 | 0.1783 |  | ~exp(b4/b3) +b1+ b2+ b3+b5 | 0.1884 | 0.1871
~exp(b1/b2) +b1+ b2+ b3+b6 | 0.1613 | 0.16 |  | ~exp(b4/b3) +b1+ b2+ b3+b6 | 0.1905 | 0.1892
~exp(b1/b2) +b1+ b2+ b3+b7 | 0.1621 | 0.1608 |  | ~exp(b4/b3) +b1+ b2+ b3+b7 | 0.1902 | 0.189
~exp(b1/b2) +b1+ b2+b3+b4+b5 | 0.1872 | 0.1857 |  | ~exp(b4/b3) +b1+ b2+b3+b4+b5 | 0.1893 | 0.1878
~exp(b1/b2) +b1+ b2+b3+b4+b6 | 0.1878 | 0.1863 |  | ~exp(b4/b3) +b1+ b2+b3+b4+b6 | 0.1909 | 0.1895
~exp(b1/b2) +b1+ b2+b3+b4+b7 | 0.1877 | 0.1863 |  | ~exp(b4/b3) +b1+ b2+b3+b4+b7 | 0.1907 | 0.1892
~exp(b1/b2) +b1+ b2+b3+b4+b5+b6 | 0.1959 | 0.1942 |  | ~exp(b4/b3) +b1+ b2+b3+b4+b5+b6 | 0.2011 | 0.1994
~exp(b1/b2) +b1+ b2+b3+b4+b5+b7 | 0.1962 | 0.1945 |  | ~exp(b4/b3) +b1+ b2+b3+b4+b5+b7 | 0.2009 | 0.1992
~exp(b1/b2) +b1+ b2+ b3+b4+b5+b6+b7 | 0.1968 | 0.1949 |  | ~exp(b4/b3) +b1+ b2+ b3+b4+b5+b6+b7 | 0.202 | 0.2
Notes: We ran a total of 171 models using all different kinds of band ratios and different mathematical relationships, including linear, logarithms, and exponentials. The above table is a sample of the models we ran, as well as the best model we found, further showing the inconsistency of the data.

## Slide 14
Methodology II
Python
Acquisition
Raw Landsat 8 OLI Image
NOAA Bathymetry Data
ArcMap
Create masks for land, clouds, shallow water and turbid water
Create two different maps
  Combine bands 5 4 3
  Normalized Differential Vegetation Index
Chesapeake Bay Chlorophyll-a Hotspot Identifier Tool
Notes: Due to this data inconsistency and a lack of time, we decided to create some visual choropleth maps using two combinations. One uses the typical 543 band combination highlighting chlorophyll, and one is a display of the NDVI of an image, calculated from bands 5 and 4. We had to mask out pixels corresponding to depths of 2 meters or less, as well as pixels corresponding to high amounts of sediment. Shallow water reflects a lot of light and can be misinterpreted as areas of high chlorophyll concentration.
Default stretches were created for the regions listed and saved as .xml files in ArcMap. These stretches can be directly applied to the final band compositions to highlight chlorophyll concentrations.

## Slide 15
Results and Conclusions
543 Color Composition
NDVI
Notes: We cross calibrated in situ data with Landsat 8 data, only to find that the data did not match up well enough to form any working algorithm. We instead created a tool that takes in raw Landsat 8 data, removes land, cloud, shallow, and high sediment concentration pixels. It then creates two images of different band combinations. The user can use these final images, apply a preconfigured stretch to the NDVI, and view chlorophyll concentrations.
The NDVI image has a 20% min clip applied to it.
Image credit: NASA DEVELOP Wise County

## Slide 16
Results and Conclusions
Notes: Our partner noticed that there are sections of the Potomac River, located north of our initial study area, that are indicating high concentrations of chl-a. Next bloom season, VIMS can include the Potomac River in their monitoring and in-situ data collecting.

## Slide 17
Uncertainties
Data not calibrated with in situ data
Maps provide relative chlorophyll-a concentrations
NDVI vs 543
Subjectivity in the stretch applied
Wolfgang Vogelbein, York River, 8-17-2015
Notes: Because the code is not calibrated with in situ data, the displayed results are only relative. They do not provide a prediction gradient. Therefore, the colored values in the images will range from low to high, no matter what the chlorophyll concentration is. For example, on a day with very little chlorophyll through out the whole bay, the areas with the most concentration will be colored red on the final images.
We’re also not sure which image results are better: The NDVI or the 543 color composition. The NDVI is meant to display vegetation, which chlorophyll fits under. The 543 color composition is also meant to display chlorophyll, but it’s typically used on land scenes. We’re not sure how it displays chlorophyll on water.
The preconfigured stretches applied to the NDVI are only a few options out of many. Since the image are visually created, they can be stretched in multiple ways, depending on how much detail is desired. It’s uncertain what the proper stretch should be.
Image credit: Provided directly from VIMS

## Slide 18
Future Work
Collect more in situ data
Calibrate Landsat 8 Data
with in situ data
Create chlorophyll-a
estimation tool for various regions
Notes: Collect more data: There are a number of reasons that we couldn’t find a good model. One reason may be that our sample size was too small. We had about 3500 data points, but compared to the whole region, this is quite small. The resolution also posed an issue. Landsat has 30m pixels, and the flowthrough data had sometimes up to ten points per landsat pixel, depending on the speed of the boat.
One other reason be that we were correlating only landsat reflectance values and in situ data. There may exist many more confounding variables, for example salinity and turbidity, that affect chlorophyll concentration. We did try to control for these, but they ended up providing us with only hundreds of data points.
The ecosystems at different locations in the whole bay are different and hold different species of chlorophyll, so a robust model may be one that is separate for each region.
More data and sampling will be necessary in order to correct for these uncertainties and create the robust model we’re looking for.
Image Credit: NASA DEVELOP Wise County

## Slide 19
Dr. Kenton Ross, NASA DEVELOP
Robert VanGundy, University of Virginia’s College at Wise
Dr. DeWayne Cecil, Global Science and Technology, Inc.
Dr. Kim Reece, Virginia Institute of Marine Science
Russ Baxter, Virginia Deputy Secretary of Natural Resources for the Chesapeake Bay
Will Hunley, Hampton Roads Sanitation Department
Todd Egerton, Old Dominion University
Advisors
Partners
Acknowledgements

## Slide 20
Acknowledgements
Others
Dr. Sarah Lubkin,
Cassandra Morgan NASA DEVELOP
Melanie Salyer, NASA DEVELOP (Wise County)