## Slide 1
Mapping Irrigation in Alabama to Improve Data Input and Model Evaluation for NASA Driven Crop-Hydrology Models
Casey Calamaio, University of Alabama in Huntsville
Samuel Ayers, University of Alabama in Huntsville
Kyle Pennington, University of Alabama in Huntsville
Alabama Agriculture:

## Slide 2: Community Concerns
Water Resource Management
  Unreported or inaccurate estimates of water withdrawals, especially from irrigation
  Water usage above 1,000 gallons should be reported to the state
Agricultural Expansion and Irrigation
  Effects of increased agriculture in Alabama on local watersheds
Crop and Hydrology Models
  Improving knowledge of where and how much irrigation exists in Alabama

## Slide 3: Project Objectives
Develop a method to statistically infer irrigated cropland from greenness indices
Edge detection and segmentation analysis to extract irrigation networks
Provide methodology and models to state institutions and NASA driven crop models

## Slide 4: Study Area
Northern Alabama and Southwestern Georgia

## Slide 5: Data Collection
Earth Observations:
  Landsat 7 ETM+ (2012)
  Advanced Spacebourne Thermal Emission and Reflectance (ASTER) (2013)
Supplemental Datasets:
  USDA Cropland Data Layer (CropScape)
  GADM Global Administrative Areas
  USDA National Agricultural Statistics
    2007 Agriculture Census
Landsat 7 ETM +
TERRA (ASTER Sensor)

## Slide 6: Methodology
Overview:
  NASS CropScape and Statistical Method:
    CropScape shows the locations and species of crops
    Used to mask Landsat 7 ETM+ NDVI
    Resulting image has a normal distribution of values
    During the 2012 drought event, NDVI values above one standard deviation are inferred as potentially irrigated crops
  Feature Extraction:
    FX classifies an image via spectral, textural, and spatial characteristics
    Spatial compactness is used to delineate circular fields
    FX toolset used on an ASTER image at 15m resolution

## Slide 7: Methodology
  Initial Observation and Acquisition
    Use Google Earth to identify center-pivot irrigation systems
      A center-pivot irrigation system waters crops via a central point which has multiple spans of sections along a radius pointing outward from the center of the circle
      Generally are the most economically feasible when used for 40-60 acres or more
      The system can be automated to move on its own
      Most center-pivot systems are designed to apply a maximum of 2 inches (gross) water per week
    Additionally located and tagged the center-pivot irrigation systems on Google Earth (pictured below: left Limestone County, right Madison County

## Slide 8: Methodology
Statistical Methodology:
NDVI and Statistical Extraction Feature Conversion and Computation
Normalized Difference Vegetation Index
Acreage Computation
  0 = Values < 1 std.
  1 = Values ≥ 1 std.
Extreme NDVI values considered as potential irrigated are one standard deviation above the mean

## Slide 9: Methodology
Feature Extraction: ENVI 5.0 FX
              ASTER Imagery over SW Georgia
              Segmentation Analysis and edge detection
              Classify image via spatial characteristics – spatial compactness for circular fields
              Establish a compactness value threshold and export resulting features
Center pivot irrigation systems

## Slide 10: Results and Discussion
Feature Extraction Results:
  2007 Agriculture Census (USDA) listed Miller County with 37, 704 acres of total irrigated cropland
  Irrigation estimates from FX are low
    Narrow search parameter and increase number of classes
    This search focused solely on center pivot irrigation

## Slide 11: Results and Discussion

## Slide 12: Results and Discussion
Example result map:
  Madison County in N. Alabama
  Total Cropland (corn, cotton, and soybean)
Red values indicate potentially irrigated crops
Total Acreage: 58,083
Potential Irrigation: 6,764 (~ 11.65%)
Known center pivot irrigation systems were detected

## Slide 13: Results and Discussion

## Slide 14: Results and Discussion
Example result map:
  Limestone County
  Total Cropland (corn, cotton,
  and soybean)
  Red values indicate potentially
  irrigated crops
  Total Acreage: 78,003
  Potential Irrigation: 11,202 (~14.36%)
  Known center pivot irrigation systems
  detected

## Slide 15: Results and Discussion
Error and Uncertainty
  FX features are trial and error in many cases
    Additional classes for Rule-Based feature extraction
      Capable of partitioning partial center pivot (3/4 or half)
      Textural and spectral properties to narrow search parameters
    Higher resolution datasets provide more accurate segmentation and will yield better results
  Inherent inaccuracy of CropScape data
    Coarse resolution of cropland data and inconsistent data values
      Automatically derived and no ground truthing
    Does not differentiate irrigated and non-irrigated cropland
      This project focused on circular fields (center pivot irrigation) because they are easily identified and were most likely in use during the 2012 drought event

## Slide 16: Conclusion
Alternative methods to identifying irrigation in Alabama is imperative to determining the actual usage of fresh water in local watersheds
This project aimed to develop a methodology to locate irrigation on a large scale
  Feature extraction and statistical analysis of crops during drought events effectively emphasized potentially irrigated fields
  These tools can help expedite more time consuming mapping techniques
Future work will emphasize narrowing the search threshold for irrigation and automate these processes
  Faster, more effective results for variable input into crop – hydrology models