## Slide 1
Results
Abstract
Objectives
Methodology
Study Area
Earth Observations
Acknowledgements
Project Partners
Team Members
Monitoring Air Quality in Shenandoah National Park to Address
National Park Service Initiatives
Using Earth Observations
Visibility calculated from AOD provides a more accurate measurement of surface visibility than visibility calculated from MERRA-2 extinction profiles.
Shenandoah National Park experiences ground-level O3 highs in late spring.
NASA Earth observations can indicate where in the atmosphere O3 originates.
NASA Earth observations can provide the park with big-picture, long-term data to foresee trends in air pollutants that affect the park; however, higher resolution imagery will provide more accurate results.
Conclusions
Air quality is considered one of Shenandoah National Park’s most fundamental resources. The park’s ecological health and visitor attendance are dependent on maintaining high air quality standards. This project utilized the NASA’s Aerosol Optical Depth (AOD), aerosol extinction profile, and Tropospheric Ozone Residual (TOR) datasets to create a long-term analysis of air quality in the park from May 2007 to August 2017. This analysis was used to identify trends in visibility and tropospheric, or ground-level, ozone throughout the park. In situ station data from Big Meadows monitoring station and 29 Automated Surface Observing System (ASOS) stations located within a 200 km radius from Shenandoah National Park were used to validate the NASA Earth observations. A tutorial on how to download, subset, and analyze TOR and AOD datasets was created to help park staff incorporate remote sensing data into their management practices related to air quality concerns. This project provided statistical and quantitative support for incorporating satellite data into Shenandoah National Park’s current air quality monitoring efforts and will aid in future decisions related to visitor education and ecological management.
Continue to introduce applications for NASA’s Earth observations to Shenandoah National Park to supplement current air quality monitoring efforts
Assess the effectiveness of current NASA satellites to measure surface visibility and ground-level ozone
Create a tutorial for park officials to help incorporate NASA Earth observations into their management decisions related to park health and air quality concerns
Display trend maps showing historic visibility and ozone levels in Shenandoah National Park
Shenandoah Health & Air Quality II
Virginia – Langley Fall 2017
Subject Matter Advisors:
Dr. Hongyu Liu, NASA Langley Research Center
Dr. Jerry R. Ziemke, NASA Goddard Space Flight Center
Science Advisors:
Dr. Bruce Doddridge, NASA Langley Research Center
Dr. Rich Ferrare, NASA Langley Research Center
Dr. Kenton Ross, NASA Langley Research Center
Partners:
Jalyn Cummings, National Park Service, Shenandoah National Park
Dr. Barkley Sive, National Park Service, Air Resources Division, Research & Monitoring Branch
Previous DEVELOP team:
Ellen Bubak, Amanda Clayton, Doug Gardiner, Nicholas Lenfant, Julie Terhune
Emily S. Doerner
Project Lead
Andrew A. Bonifas
James Ficklin
Nick Gulston
Roger Johnson
Sarah K. Philips
Chart: Comparison of Average Monthly Ozone (O3)
Chart: MERRA-2 AOD Visibility Correlation
High O3
75 ppbv
Low O3
60 ppbv
TOR in ppbv
Poor
Visibility
0 km
Good
Visibility
150 km
Visibility: June 10, 2015 Case Study
Correlation between in situ and satellite measurements:
R = 0.526
National Park Service, Shenandoah National Park
National Park Service, Air Resources Division, Research & Monitoring Branch
Terra MODIS
Aqua MODIS
Ozone: June 2007 and 2016
TOR in ppbv
CASTNET (ozone measurements); Tropospheric Ozone Residuals (TOR); IMPROVE and ASOS (in situ visibility measurements); Aqua & Terra MODIS AOD; MERRA-2 extinction profiles
Convert TOR, MODIS, MERRA-2 into GIS-ready formats; extract 1pm timeframe for ASOS; Convert TOR Dobson units to ppbv
Compare Earth observations and model-based estimations of visibility with ASOS reference data; create time series and trend maps
Data Acquisition
Data Processing
Data Analysis
2007
2016
R = 0.514
Shenandoah Airshed
Shenandoah National Park Boundary
MERRA-2 Extinction Profile
MERRA-2 AOD
MODIS AOD