## Slide 1
NASA Ames Research Center
Monitoring drought conditions in the Navajo Nation using NASA Earth observations
Navajo Nation Climate II
.
Navajo Technical University
Navajo Nation Department of Water Resources: Water Management Branch
Dr. Jay W. Skiles, NASA Ames
Dr. Venkat Lakshmi, University of South Carolina
Clayton Sodergren
Amber Brooks, Chippie Kislik and Andrew Nguyen, NASA
DEVELOP National Program.
Use images.
Make sure that it has some sort of flow, that it makes sense. Show your results in a logical order.
No bullets.
Use bullets.
Use complete sentences with periods.
The Navajo Nation, a 65,700 km2 Native American territory located in the southwestern United States, has been increasingly impacted by severe drought events and changes in climate. These events are coupled with a lack of domestic water infrastructure and economic resources, leaving approximately one-third of the population without access to potable water in their homes. Current methods of monitoring climate and drought are dependent on national-scale state-based monthly drought maps calculated by the Western Regional Climate Center. These maps do not provide the spatial resolution needed to illustrate differences in drought severity across the vast Nation. To better understand and monitor drought events and drought regime changes in the Navajo Nation, this project investigated methodologies to create a tool that calculates Standard Precipitation Index rasters for the study area, and created a geodatabase of historical climate information for use by the tool. The tool and geodatabase use Tropical Rainfall Monitoring Mission observed precipitation data and Parameter-elevation Relationships on Independent Slopes Model modeled historical precipitation data. These products allow resource managers in the Navajo Nation to utilize current and future NASA Earth observation data for increased decision-making capacity regarding future climate change impact on water resources.
Create a Standardized Precipitation Index tool specific to Navajo Nation boundaries
Compare SPI drought intensity to other climate variables in the area
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Cheryl Cary1,6 (Project Lead), Michael Gao2,6, Vickie Ly3,6, Anton Surunis4,6, Sophie Turnbull-Appell5,6
1University of California, Santa Cruz; 2Johns Hopkins University; 3University of California, Berkeley; 4University of California, Davis; 5University of California, Los Angeles; 6DEVELOP National Program
Figure 1: Study area map
Global Precipitation Monitor (GPM)
The Navajo Nation is a 65,700 km2 Native American territory. The project used USGS Hydrologic Unit Code 8 (HUC 8) watershed boundaries that intersect with the political boundary of the Nation.
Monthly Accumulated Rainfall Rasters
User -chosen SPI Algorithm
SPI Rasters
SPI Rasters
Zonal Statistics
Boundary Specific SPI:
Average SPI values for a
user chosen polygon
ex. 6-, 9-,
12-month SPI
-1.7
-0.6
-1.4
-0.9
-1.2
SPI Raster Calculation:
Tropical Rainfall Monitoring Mission (TRMM)
Vickie Ly, Michael Gao, Anton Surunis,
Cheryl Cary (Project Lead), Sophie Turnbull-Appell