## Slide 1
North Carolina – NCEI
OHIO RIVER BASIN
Water Resources
Monitoring Flash Drought Potential and Quantifying the Hydrologic Impacts in the Ohio River Basin Utilizing NASA Earth Observations
Adelaide Schmidt, Isabelle Runde, Jessica Ganim, & Kayleigh DeBruyne

## Slide 2
Study Area
Ohio River Basin
Provides freshwater resources
Major agricultural producer
Main crops
Moisture rich environment
0
100
200
400
Miles
Kilometers
0
100
200
400
Ohio River Basin
State Boundary
OHIO RIVER BASIN
LAND COVER
Corn
Grain Crops
Soybeans
Other Crops
Fallow/Idle Cropland
Developed
Barren
Forest
Grassland/
Pasture
Wetlands
SOURCE: National Cropland Dataset 2019
Manufacturing
Energy
Recreation
Agricultural industries
OH, KY, IL, TN rank in the top 10 states by number of farms
Soybeans, corn, small grains
Notes: Our study area is the Ohio River Basin, a watershed in the Midwest/southeast that intersects 11 states. Our focus was on the 7 states that comprise the majority of the ORB – IL, IN, OH, PA, WV, KY, TN.
The basin provides freshwater resources for a variety of sectors including manufacturing, energy, recreation and agricultural.
The watershed is a major agriculture producer with almost 50 million acres in farms (48,240,073) and includes 4 of the top ten states in the US of farms per state, with IL and IN in the top 10 agriculture producing states grossing over $10 billion each. According to 2017 Census of Agriculture, the annual market value of agricultural products in KY alone is over $5 billion.
The major crops are soybeans, corn and small grains (wheat, barley, oats, rye).
Source: USDA 2017 Census of Agriculture
The Ohio River basin includes the climate transition zone between the humid continental and humid subtropical zones. This creates a moisture rich environment that is important to consider when talking about drought. The ORB has also seen general trends in increasing temperature and increasing annual precipitation.
Source: OHIO RIVER BASIN – Formulating Climate Change Mitigation/Adaptation Strategies through Regional Collaboration with the ORB Alliance
SOURCE National Cropland Dataset 2019

## Slide 3
Flash Drought
PERSISTENT
ATMOSPHERIC
ANOMALIES
Higher temperatures
More sunny days
Stronger winds
Larger vapor pressure deficits
INCREASED EVAPORATIVE DEMAND
Increased temperature anomalies
Drier topsoil
Moisture depletion at depth
ET increases
(meet atmospheric demand)
ET decreases
(vegetation decreases water usage)
DECREASED SOIL MOISTURE & AGRICULTURAL DROUGHT
Vegetation appearance changes once rootzone soil moisture falls below threshold
ET anomaly transitions from positive to negative
Surficial evaporation increases
Flash Drought Evolution
Reduced evaporative cooling
Develops rapidly in a few weeks
Driven by precipitation deficits combined with extreme weather anomalies
Leads to decreased soil moisture and vegetation stress
TIME
Notes: A term that started to show up around the 2000s and became popularized surrounding drought events in 2011-12, flash drought is a drought that develops very rapidly over the course of a few weeks. While low precipitation is a factor, as with all droughts, the key to flash drought is that these average to below average precipitation levels are coupled with persistent atmospheric anomalies such as higher temperatures, stronger winds, or more sun.
These drivers lead to increased evaporative demand, which can be described as the thirst of the atmosphere. This has multiple effects:
- Surficial evaporation increases leading to drier topsoil
- to meet this demand, ET also increases thus depleting soil moisture at lower depths
- As the moisture in the environment decreases there is a shift to a water-limited system which causes ET to decrease and vegetation stress increases
Flowchart generated by DEVELOP team.

## Slide 4
Community Concerns
HAB in Maumee River, OH
Image: Aerial Associates Photography, Inc. by Zachary Haslick
Flash Drought Impacts:
Agricultural losses
Increased wildfire risk
Increase in harmful algal blooms (HAB)
Intensifying cycles of excess moisture followed by drought in the region
Growing interest to apply newly developed flash drought indicators to water resource monitoring
2012 flash drought cost over $30 billion
Image: Kentucky Climate Center
Notes: Flash droughts are a growing concern in the ORB community. The patterns of excess moisture followed by drought the area has seen recently are expected to continue and intensify. This concerns forecasters, as flash drought is an understudied phenomenon and they want more tools to predict the onset of flash drought
Flash drought can have serious impacts on communities and its nature of agricultural drought has particularly harmful effects on the agricultural community. Knowing how prominent agriculture is in the ORB this is a strong concern.
In 2012, there was a large flash drought across much of the US. It developed over just two months during the growing season and resulted in over $30 billion losses in the agricultural sector (Otkin et al., 2018; National Centers for Environmental Information, 2017).
Other associated impacts flash drought can have include an increased risk for wildfires and increases in HABs.
Image (left): Courtesy of Kentucky Climate Center
Image (right): Flickr. Aerial Associates Photography, Inc. by Zachary Haslick. Maumee River HABs Sept 22 2017 2298. Public Domain Mark 1.0. https://www.flickr.com/photos/noaa_glerl/36621364324/in/photolist-YNDdSS-XRCQoR-XRCPEX-XRCMTk-XN74GL-XRCQrM-BLLUVf-BLLUz5-BLLW85-BLLWaE-BLLUqC-XRCQAp-BLLWdL-BLLTTL-YNDeg7-XRCMQ4-YNDdtL-YNDe2j-XN74Kb-YNDdwb-XRCQEH-XRCQya-YNDdZq-XN73cw-XRCMVz-9UhCu2-ejuTXG-ejuU91-ejpb8M-ejpbok-RXniWs-7dbEmf-RXn3Hb-Sx9QgH-RXmGQq-SikAZm-SxaFni-Ri7kxz-SxaFFz-Ri7EAe-SikBos-Ri7jQH-Ri7Ej2-SikfQy-Sike8L-RXnpsC-SikiZj-SikiBA-RXmZDA-SikAgY/

## Slide 5
Project Partners
Image: Eden, Janine, and Jim
Ohio River
Image: Ken Lund
Kentucky Climate Center
Provides forecasting and early drought warning
Houses the KY Mesonet
Distributes data and data-derived products to stakeholders
NOAA National Weather Service, Ohio River Forecast Center
Produces meteorological and hydrological products
Provides impact-based decision support
Water resource outlooks
Drought briefings
Image: Scott Beale / Laughing Squid
Notes: To address some of the community concerns around flash drought in the ORB we are partnering with two organizations that work on weather forecasting and provide climate information to the public and stakeholders.
We are working with the state climatologist at the Kentucky Climate Center. The KY Climate Center, at Western Kentucky University, houses the Kentucky Mesonet, a weather and climate data network of 74 stations across the state. They work in areas of water management, drought early warning, and forecasting. They distribute data and data-derived products on their website and also through a mobile app. These outlets allow for the distribution of information to various stakeholders and decision-
makers across the state, including those in government, water management, and farming communities.
(Mahmood, Schargorodski, Foster, & Quilligan, 2019).
We also partnered with a hydrologist at NOAA National Weather Service, Ohio Forecast Center (ORFC).They produce a variety of weather and hydrological information products
involving precipitation and water resources outlooks. These include streamflow forecasts and drought briefings. They disseminate climate and forecasting information to provide impact-based decision support to the public.
Both organizations were interested in developing a product that utilizes various drought indices to build confidence in their ability to accurately inform stakeholders of drought risk. They currently rely heavily on the Standardized Precipitation Index (SPI), an entirely precipitation-based drought index, to identify drought and to develop the appropriate warnings. SPI, however, does not incorporate evapotranspiration, which, as we just learned, is a key process associated with flash drought onset and evolution.
Image: Flickr. Scott Beale / Laughing Squid. The Ohio River. CC BY-NC-ND 2.0 https://www.flickr.com/photos/laughingsquid/15574742699/in/faves-187233743@N05/

## Slide 6
Objectives
Compare drought index products to identify potential leading and reacting flash drought indicators
Investigate environmental hydrologic response through soil moisture observations to better understand nature of flash drought in ORB
Demonstrate the use of SMAP-derived soil moisture to enhance in situ data observations in Kentucky
Image: Kentucky Climate Center
Notes: Based on the needs of our project partners and the DEVELOP program, we outlined 3 main objectives for the project.
Image (top): Produced by NASA DEVELOP
Image (middle): Courtesy of Kentucky Climate Center
Image (bottom): NASA

## Slide 7
Analysis Components
1. Drought Indicator Analysis
A. 2019 September Flash Drought Case Study
  June 01 – October 31 2019
  B. Decadal Time Series (TS)
  January 01 2010 – December 31 2019
2. Soil Moisture Analysis
A. Kentucky Mesonet and SMAP soil moisture
July 01 – October 31 2019
Image: Kentucky Climate Center
Notes: Our analysis was broken up into two different components.
Image: Courtesy of Kentucky Climate Center

## Slide 8
NASA Earth Observations
Soil Moisture Active Passive
(SMAP)
Terra MODerate Resolution Imaging Spectroradiometer (Terra MODIS)
Level 4 gridded surface (5 cm) soil moisture
Thermal imagery used to compute evapotranspiration fraction for LERI
Notes: In this study we used two different NASA satellites and sensors.
SMAP was used to collect remotely sensed soil moisture and MODIS provided land surface temperature that was used as an input for the LERI drought index.
Image (left, right): NASA

## Slide 9
1. DROUGHT INDICATOR ANALYSIS

## Slide 10
Drought Indicators
Index | Physical Measurement | Output | Grid
Landscape Evaporative Response Index | Terra MODIS land surface temperature | actual evapotranspiration (ETa) anomaly 2000 – 2019 | 1 km
Evaporative Demand Drought Index | NASA National Land Data Assimilation Systems (NLDAS-2) temperature, humidity, wind speed, & solar radiation | evaporative demand (E0) anomaly 1980 – 2019 | 12 km
Standardized Precipitation-Evapotranspiration Index | NOAA NCEI nClimGrid precipitation and temperature | water balance standardized 1895 – 2019 | 5 km
Standardized Precipitation Index | NOAA NCEI nClimGrid precipitation | precipitation standardized 1895 – 2019 | 5 km
EDDI
SPEI
SPI
LERI
Notes: Drought indices are used by forecasters to detect and predict droughts. Indices quantitatively categorize drought by combining data from one or more indicators, such as precipitation or evapotranspiration to look for signals of drought (Zargar, Sadiq, Naser, &amp; Khan, 2011).
For our study we focused on 4 indices, including industry standards like SPI as well as newer indices such as LERI and EDDI.
Our partners traditionally use SPI, however it solely considers precipitation and is only available in 1-month or longer products, which in the moisture rich environment of the ORB and considering the rapid onset of flash drought may not be the most useful.
Therefore, our project partners were particularly interested in looking into EDDI and LERI due to them being more recent and their potential for flash drought detection. These indices use input parameters such as temperature, evapotranspiration and wind speed which are some of those persistent weather anomalies we highlighted earlier that can lead to flash drought. They are also available on a shorter time scale.

## Slide 11
1. Resample to 12 km grid
1. DROUGHT INDICATOR ANALYSIS
Methods
Acquisition
Processing
MONTHLY PRODUCTS
EDDI 1 - MO
LERI 1 - MO
SPEI 1 - MO
SPI 1 - MO
SPI 3 - MO
SPEI 3 - MO
WEEKLY PRODUCTS
EDDI 1 - WK
EDDI 2 - WK
LERI 8 - DAY NAC
LERI 8 - DAY AC
Notes: To analyze how different indicators performed throughout the 2019 flash drought, we downloaded the data for different indices and their various products. First, we resampled to the 12 km grid – EDDI has the coarsest resolution

## Slide 12
1. Resample to 12 km grid
1. DROUGHT INDICATOR ANALYSIS
Methods
Acquisition
Processing
2. Crop to region of interest
MONTHLY PRODUCTS
EDDI 1 - MO
LERI 1 - MO
SPEI 1 - MO
SPI 1 - MO
SPI 3 - MO
SPEI 3 - MO
WEEKLY PRODUCTS
EDDI 1 - WK
EDDI 2 - WK
LERI 8 - DAY NAC
LERI 8 - DAY AC

## Slide 13
1. Resample to 12 km grid
1. DROUGHT INDICATOR ANALYSIS
Methods
Acquisition
Processing
2. Crop to region of interest
MONTHLY PRODUCTS
EDDI 1 - MO
LERI 1 - MO
SPEI 1 - MO
SPI 1 - MO
SPI 3 - MO
SPEI 3 - MO
WEEKLY PRODUCTS
EDDI 1 - WK
EDDI 2 - WK
LERI 8 - DAY NAC
LERI 8 - DAY AC
3. Reclassify to USDM categories:
USDM | Z-SCORE | PERCENTILE
ND | -0.4 or greater | 31 to 100
D0 | - 0.5 to -0.7 | 21 to 30
D1 | - 0.8 to -1.2 | 11 to 20
D2 | -1.3 to -1.5 | 6 to 10
D3 | -1.6 to -1.9 | 3 to 5
D4 | -2.0 or less | 0 to 2
Notes: Cite to USDM The U.S. Drought Monitor (USDM) categorizes drought into 6 groups that correspond to an index’s z-score or percentile value. The drought categories are:
ND – No Drought
D0 – Abnormally Dry
D1 – Moderate Drought
D2 – Severe Drought
D3 – Extreme Drought
D4 – Exceptional Drought

## Slide 14
2019 Results
EDDI 1 MO LERI 1 MO SPI 1 MO SPI 3 MO SPEI 1 MO SPEI 3 MO
OCT
SEP
AUG
JUL
D0
D1
D2
D3
D4
ND

## Slide 15
2019 Results
EDDI 1MO
LERI 1MO
SPEI 1MO
SPEI 3MO
SPI 1MO
SPI 3MO
Jul
0
10
20
30
40
50
60
70
80
90
100
EDDI 1MO
LERI 1MO
SPEI 1MO
SPEI 3MO
SPI 1MO
SPI 3MO
Aug
EDDI 1MO
LERI 1MO
SPEI 1MO
SPEI 3MO
SPI 1MO
SPI 3MO
Sep
EDDI 1MO
LERI 1MO
SPEI 1MO
SPEI 3MO
SPI 1MO
SPI 3MO
Oct
D0
D1
D2
D3
D4
ND
2019 Regional drought classification by month
Percent area (%)

## Slide 16
TS Results
EDDI 1 MO
LERI 1 MO
SPEI 1 MO
SPI 1 MO
SPEI 1 MO
SPEI 3 MO
SPI 1 MO
SPI 3 MO
2011
2013
2015
2017
2019
2011
2013
2015
2017
2019
HUC4 0505
Kanawha
% area >= D3
0
50
75
100
25
% area >= D3
0
50
75
100
25

## Slide 17
TS Results
EDDI 1 MO
LERI 1 MO
SPEI 1 MO
SPI 1 MO
SPEI 1 MO
SPEI 3 MO
SPI 1 MO
SPI 3 MO
2011
2013
2015
2017
2019
2011
2013
2015
2017
2019
% area >= D3
0
50
75
100
25
% area >= D3
0
50
75
100
25
HUC4 0513
Cumberland

## Slide 18
Discussion & Conclusions
EDDI displays sensitivity – represents potential evapotranspiration, which frequently changes according to meteorological variations
LERI has a shorter reference period and does not have a D4 equivalent
SPI and SPEI 1-month products capture the observed severity of the 2019 flash drought
September 2019 SPI and SPEI 3-month products reflect local knowledge of the spatial distribution of initial drying

## Slide 19
2. SOIL MOISTURE ANALYSIS

## Slide 20
Kentucky Mesonet
Measures surface soil moisture (2, 4, & 8 inches)
30-minute intervals at 42 stations
Stevens Digital Hydraprobe-II sensors
Kentucky Climate Center Soil Moisture Monitoring Stations:
Notes: This current map will be changed to be editable – generated by DEVELOP team.

## Slide 21
Methods
Study Period:
July-October 2019
Time Scale:
Weekly,
Biweekly,
Monthly
1) Mesonet dataset converted to spatial data frame
2) Values extracted from SMAP raster layer
3) Medians computed for 5-cm SMAP and 2-, 4-, & 8-inch Mesonet
5) RMSE computed for daily time scale
6) 3-day & 7-day rolling means
4) Time series plots & soil descriptions data table
7) Soil texture comparison to RMSE
DATA ACQUISITION
DATA VISUALIZATION
DATA ANALYSIS
2. SOIL MOISTURE ANALYSIS

## Slide 22
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
HARD
SMAP vs. Mesonet Daily Surface Soil Moisture
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
PVRT
SMAP vs. Mesonet Daily Surface Soil Moisture
Daily time series of 5-cm SMAP, 2-inch Mesonet, 4-inch Mesonet, and 8-inch Mesonet from July 1-October 31, 2019 at four sample Mesonet stations (PVRT, FCHV, HARD, and LXGN)
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
LXGN
SMAP vs. Mesonet Daily Surface Soil Moisture
0.2
0.3
0.4
0.5
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
FCHV
SMAP vs. Mesonet Daily Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
Surface Soil Moisture Comparisons
Notes: -These selected sites show similar values of surface soil moisture up to 8 inches
-Each site shows similar trends of wetness and dryness between 5-cm SMAP, 2-inch Mesonet, 4-inch Mesonet, & 8-inch Mesonet

## Slide 23
Time series of 5-cm SMAP and 2-inch Mesonet 3-day rolling means from July 1-October 31, 2019 at four sample Mesonet stations (PVRT, FCHV, HARD, and LXGN)
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
PVRT
SMAP vs. Mesonet 3-Day Rolling Means
0.20
0.25
0.30
0.35
0.40
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
FCHV
SMAP vs. Mesonet 3-Day Rolling Means
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
HARD
SMAP vs. Mesonet 3-Day Rolling Means
0.1
0.2
0.3
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
LXGN
SMAP vs. Mesonet 3-Day Rolling Means
Data Product
2-inch Mesonet
5-cm SMAP

## Slide 24
Daily time series of 5-cm SMAP, 2-inch Mesonet, 4-inch Mesonet, and 8-inch Mesonet from July 1-October 31, 2019 at three sample Mesonet stations (FARM, GAMA, and WNCH)
0.1
0.2
0.3
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
GAMA
SMAP vs. Mesonet Daily Surface Soil Moisture
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
WNCH
SMAP vs. Mesonet Daily Surface Soil Moisture
0.0
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
FARM
SMAP vs. Mesonet Daily Surface Soil Moisture
Data Product
2-inch Mesonet
4-inch Mesonet
8-inch Mesonet
5-cm SMAP
Notes: -These sites show similar trends of wetness and dryness between SMAP and each Mesonet soil depth
-We can observe that values at different depths are different, but we do similar patterns of wetness and dryness

## Slide 25
Time series of 5-cm SMAP and 2-inch Mesonet 3-day rolling means from July 1-October 31, 2019 at three sample Mesonet stations (FARM, GAMA, and WNCH)
0.1
0.2
0.3
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
5-cm SMAP
GAMA
SMAP vs. Mesonet 3-Day Rolling Means
0.0
0.1
0.2
0.3
0.4
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
Data Product
2-inch Mesonet
5-cm SMAP
FARM
SMAP vs. Mesonet 3-Day Rolling Means
0.1
0.2
0.3
Jul
Aug
Sep
Oct
Nov
Time
Surface Soil Moisture
WNCH
SMAP vs. Mesonet 3-Day Rolling Means
Data Product
2-inch Mesonet
5-cm SMAP

## Slide 26
Soil Texture Comparisons
0.02
0.03
0.04
0.05
0.06
0
20
40
60
80
Soil Texture (%)
RMSE
Clay
Soil Texture Analysis
0.02
0.03
0.04
0.05
0.06
0
20
40
60
80
Soil Texture (%)
RMSE
Silt
Soil Texture Analysis
0.02
0.03
0.04
0.05
0.06
0
20
40
60
80
Soil Texture (%)
RMSE
Sand
Soil Texture Analysis
Figures 15-17. Percent silt, sand, & clay vs. RMSE derived from pedon descriptions and regression model of 2-inch Mesonet (x value) and 5-cm SMAP (y value) across 22 Mesonet stations from July 1 through October 31, 2019
Blue Grass Region
Mississippi Embayment
Mississippian Plateaus
Western KY Coal Field
Notes: -representation of sites per Physiographic region of Kentucky is disproportionate
-While it is evident that each station is majority silt, there is no observed relationship between RMSE and soil texturetherefore,
No observed relationship between SMAP and Mesonet comparisons when analyzed with soil texture/don’t see one classification showing stronger matching than the other

## Slide 27
Discussion & Conclusions
SMAP varies in representation of actual soil moisture across 35 sites
SMAP and Mesonet measurements exhibit similar patterns of wetting & drying
Wetting and drying patterns reflect patterns of categorical drought changes
Soil textural class has no observable relationship with SMAP and Mesonet comparison
Notes: SMAP and Mesonet measurements exhibit similar patterns of wetness & dryness regardless of quantitative variations

## Slide 28
Future Work
Create composite drought indicator that balances the strengths of each index
Analyze 2012 and 2016 drought events to detect spatial distribution of drought evolution
Examine time series of sub-monthly SPI
Extend gridded SMAP and other gridded soil moisture products analysis to 2012 and 2016 events
Image: Kentucky Climate Center
Notes: Image: Courtesy of Kentucky Climate Center

## Slide 29
Stuart Foster
Kentucky Climate Network
James Noel
NOAA NWS Ohio River Forecasting Center
Ronald Leeper
Science Advisor, NOAA NCEI, North Carolina Institute for Climate Studies
Rocky Bilotta
NOAA NCEI, Center for Weather and Climate
      Andrew Shannon
NASA DEVELOP NC – NCEI Fellow
Jordan Basham
Western Kentucky University PBS
Image: Arthur LaBar
Notes: We would like to acknowledge a few people in particular who contributed their knowledge, time, insights, and support to make this project possible. Thank you.
Image: Flickr. Arthur T. LaBar. Barn, Albany, Kentucky. CC BY NC 2.0. https://www.flickr.com/photos/arthurtlabar/40239915444/in/faves-187233743@N05/