## Slide 1
Wetland ecosystems are annually or seasonally wet transition zones between land and water. They provide a range of ecosystem services such as water filtration, flood mitigation, and carbon sequestration, as well as hosting biodiversity hotspots. Although they fulfill fundamental physical and natural processes, wetland extent and health are threatened by anthropogenic influences related to urbanization, population increase, pollution, and climate change. Recognizing the need to quantitatively monitor changes in these recently threatened ecosystems in a timely and cost-effective way, we developed a Google Earth Engine (GEE) Python API tool for automated wetland extent mapping using optical and radar satellite sensors that can be applied globally. The tool will significantly improve wetland change analysis and monitoring as the optical and SAR data proves high resolution (5-10 m) imagery, and SAR data is unaffected by cloud cover and light availability (day vs. night), which are common limitations for other remotely sensed sensors. The tool utilizes Copernicus Sentinel-1 C-band and NISAR L-band synthetic aperture radar (SAR) imagery. During image preprocessing, we applied a MODIS snow mask product to mask global snow coverage, which would affect land classification sensitivity. Calibration and validation were conducted through a historical change and sensitivity analysis of the Sudd watershed located in central Sudan. The tool was the first of its kind, as it enables NISAR data processing through an open-source GEE repository, further expanding and improving the utility of NASA Earth observations and contributing to NASA Open Science initiatives. We anticipate the tool will be used by researchers and practitioners interested in wetland monitoring and management..
Abstract
Develop a tool to quantify wetland extent on a global scale using Google Earth Engine in the Python API
Create user-friendly interface for visualizing and analyzing wetland extent
Improve remote sensing applications for water resources using optical and SAR sensors
Establish a methodology that can easily integrate NISAR products upon launch
Objectives
Methodology
Earth Observations
Results
Developed a user-friendly tool for regional wetland inundation assessment
Contributed to a dense time series used for detecting wetlands, a particularly important application during rainy seasons
The WET 3.0 tool will implement and utilize future NISAR data with current Sentinel-1 data
Promoting the use of the Python API will allow users to eventually move off of Google Earth Engine and use other open-source platforms through the use of Python
Conclusions
Acknowledgements
Team Members
Lori Berberian
(Project Lead)
Kaely Harris
Mitch Porter
Emma Waugh
California – JPL
WET Water Resources
A Google Earth Engine Python API Tool to Automate Wetland Extent Mapping Using Radar Satellite Sensors for Wetland Management and Monitoring
South Sudan
White Nile River
Sudd Wetland
0
100
200 km
INPUT
PROCESSING
CLASSIFICATION
OUTPUT
ANALYSIS
Sentinel-1 C-SAR
NISAR*
Terra MODIS
VIIRS data from Downs et al. 2023
filter by date and ROI
snow mask
de-speckle
calculate VV/VH ratio
calculate mean pixel values
classify study area
accuracy assessment
departure from mean
final classification
inundation thresholds
Sentinel-1 C-SAR​
Terra MODIS
NISAR (set to launch in 2024)
Sentinel-2
The team would like to show our gratitude to Bruce Chapman, Ben Holt, and Michael Pazmino at (NASA Jet Propulsion Laboratory) for their contributions to this technology and innovation project. We would also like to recognize the Wetlands Water Resources 2.0 team, and Brandi Downs et al. (2023). This material contains modified Copernicus Sentinel data processed by ESA, Dynamic World V1 data produced by Google in partnership with National Geographic Society and the World Resources Institute, and MODIS Terra data processed by NASA National Snow and Ice Data Center
Satellite image of the Sudd Wetland in October 2018
Study Area
Sudd Wetland, South Sudan
Test the precision and accuracy of our tool against Downs et al. 2023, a wetlands classification study conducted across South Sudan.
Understand a regionally important freshwater environment
VV Pixel Values
0 2000 6000 10000
0 0.2 0.4 0.6 0.8 1.0
VH Pixel Values
0 2000 4000 6000 8000
0 0.02 0.04 0.06 0.08 0.10
open water
trees
grass
shrub & scrub
inundated vegetation
We obtained thresholding values for land classification by drawing training polygons based on known land cover from the Dynamic World land cover product and plotting histograms of each land cover type. Backscatter threshold values selected by histogram analysis are approximately an order of magnitude difference for VV and VH bands.
open water
no water
inundated vegetation
Classified Image
Sentinel-1 C-SAR VV Image
October 16, 2021
Backscatter
0.5
0
VV threshold values are dark water < 0.01 < inundated vegetation < 0.11 < no water. VH threshold values are dark water < 0.0015 < inundated vegetation < 0.011 < no water. The threshold values were applied to classify wetland inundation extent from Sentinel-1 imagery.
Suomi-NPP VIIRS