## Slide 1: Los Angeles Health & Air Quality Identifying Urban Emission Patterns in the Los Angeles Megacity
NASA DEVELOP Showcase
Washington, D.C.
July, 30th 2015
Photo by DAVID ILIFF. License: CC-BY-SA 3.0
Talha Rafiq (Project Lead)
Isis Frausto-Vicencio
Valerie Carranza

## Slide 2: Megacities Carbon Project
Photo by JPL Megacities Carbon Project
Notes: 40% of CA population resides in LA
Methane is 21 times more global warming potential than CO2
A better understanding of methane is needed

## Slide 3: Objectives
Compare our bottom-up method with top-down NASA Earth observations: HyTES and CLARS
Research
Obtain and formulate emission factors for the top CH4 producing sectors
Compare
Develop
Develop a raster-based spatial representation of CH4 emissions in the SoCAB region
Notes: Our research presents a bottom-up approach to mapping methane distribution for the LA megacity
HyTES = hyperspectral thermal emissions spectrometer (on a plane)
CLARS= California Laboratory for Atmospheric Remote Sensing

## Slide 4: Methodology
Data Collection of Methane Sectors
Process & Validate
Research & Rank of CH4 Emission Sectors using studies from California AIR Resources Board (CARB)
Convert all data into 3km by 3km grid cell raster visualization
Rank | Source | SoCAB Total (Gg CH4/year)
1 | Landfills | 171.3
2 | Oil & Natural Gas | 87.4
3 | Livestock-Dairy | 77.3
4 | Wastewater Treatment Plants | 56.3
CARB 2012 | SoCAB (projected)

## Slide 5: Methodology

## Slide 6
1
Notes: Landfill data gathered from the California Department of Resources, Recycle, and Recovery, 84 landfills in SoCAB, 21 active, 59 closed, 1 closing, 3 inactive, landfill emissions data is calculated using
Landfill with the highest output was the Puente Hills Landfill in Los Angeles County at 922,333 CO2 Equivalent emissions in 2012

## Slide 7
2
Notes: Oil Wells: 28915; 5585 active, 23330 plugged and abandoned; California Department of Conservation
Division of Oil, Gas, and Geothermal Resources
NG Pipelines: 1067; storage distribution, and transmission; National Pipeline Mapping System

## Slide 8
3
Notes: 158 dairies in Chino/Ontario Area
122 Riverside Dairies

## Slide 9
Notes: And when you overlay all three types of sectors together, here’s what it looks like! The range from most emissive which is red to least emissive which is blue

## Slide 10: Future Research
Comparison of this bottom-up method to top-down NASA Earth Observations
In-situ network
OCO-2
TCCON
JAXA GOSAT