## Slide 1
Monitoring Runoff Plumes Originating from the Tijuana River Estuary To Inform Water Quality Management
Improve the monitoring of pollution plumes along the southern California coast by incorporating remote sensing capabilities
Create a tool that can delineate pollution plumes from satellite imagery in GEE
Assess water quality parameters, such as turbidity and colored dissolved organic matter (CDOM)
Evaluate the effectiveness of using satellite imagery to estimate water quality parameters
Objectives
Methodology
Earth Observations
Turbidity thresholds to map mixed, storm, and wastewater plumes extent were established
Stormwater plumes tend to be larger and have more severe water quality indexes
Remotely-sensed data accurately estimates turbidity and chlorophyll-a.
Remotely sensed data more accurately estimates turbidity for stormwater than wastewater.
Further analysis is need to evaluate measuring CDOM with remote sensing.
Conclusions
The San Diego Water Resources Team would like to thank Dr. Juan Torres-Pérez, Dr. Daniel Sousa, Dr. Christine Lee, Benjamin Holt, Dr. Kenton Ross, Mariam Ayad, Britnay Beaudry, and Lisa Tanh on their guidance, constructive feedback, time, and support throughout this project. We would also like to acknowledge former DEVELOPers Hayley Pippin, Arbyn Olarte, Roxana Pilot, and Vanessa Valenti for developing the ORCAA tool.
This material contains modified Copernicus Sentinel data (2017-2022), processed by ESA.
Acknowledgements
Project Partners
Team Members
Ethan Gates
Project Lead
Max VanArnam
Jonathan Szeto
Stefanie Mendoza
Storm and wastewater runoff are large sources of pollutant discharge along the southern California coast and are major concerns pertaining to the health of local communities and ecosystems. However, studying the deteriorated water quality caused by these events along the coasts can be difficult given the dynamic nature of winds and currents. This project utilized satellite imagery and the Optical Reef and Coastal Area Assessment (ORCAA) Google Earth Engine tool to visualize and analyze the water quality of the San Diego coast after major storm and wastewater events as an alternative for in-situ sampling. Using Landsat 8 Operational Land Imager (OLI) and Sentinel-2 Multispectral Instrument (MSI), the team analyzed the extent of pollution plumes released from the Tijuana River Estuary from 2013 to 2022 and estimated water quality parameters, such as colored dissolved organic matter (CDOM). Remotely-sensed turbidity, chlorophyl-a, and CDOM were also cross validated with in-situ data from NOAA and the San Diego Public Utilities in the San Diego coastal area to evaluate the accuracy of water quality data derived from satellite imagery.
Abstract
Node Location
San Diego Coast Water Resources
California – Ames
Plume Type | Turbidity Thresholds | Area (mi2) | CDOM (m-1) | Turbidity (FNU/NTU) | Chlorophyll-a (µg/L)
Storm | 3.48 | 4.18 | 1.04 | 5.59 | 5.26
Waste | 1.44 | 3.17 | 0.12 | 5.06 | 1.85
Mixed | 1.86 | 4.18 | 0.34 | 5.29 | 2.89
San Diego Regional Water Quality Control Board
Water Keeper Alliance
Tijuana River National Estuarine Research Reserve
City of San Diego and City of Imperial Beach
Conditions | Equation | R2 | Sample Size (n)
CDOM (all) | 0.804x + 1.64 | 0.097 | 28
Chl-a (all) | 0.772x + 4.79 | 0.47 | 10
Turbidity (all) | 13.2x - 36.1 | 0.73 | 75
Turbidity (Stormwater) | 16.0x - 64.4 | 0.73 | 19
Turbidity (Wastewater) | 0.0930x + 2.51 | 0.030 | 35
Turbidity (Mixed) | 1.56x + 0.517 | 0.20 | 23
~5 days, 10-20m, 2018 +
~16 days, 15-100m, 2013 +
Landsat 8 Operational Land Imager
Level 2 Surface Reflectance Tier 1
Sentinel-2 Multispectral Instrument
Level 2A Surface Reflectance
Brown Field Municipal Airport Precipitation Station
International Wastewater Treatment Plant
San Antonio de los Buenos Wastewater Treatment Plant
Cities
Offshore water sampling site
Boca Rio Water Quality Station
Tijuana River Valley
Tijuana River Watershed
Ocean
Tijuana River
U.S-Mexico Border
Results
Study Area
San Diego
Tijuana
Remotely-sensed Turbidity (FNU)
In-situ Turbidity (FNU)
y = 13.2x – 36.1
R2 = 0.73, n = 75
Earth Observations
Landsat 8 OLI, Sentinel-2 MSI
Maps of plumes
Delineate plume extent in GEE using turbidity thresholds
Regression models
GEE Tutorial
Match remotely sensed data with in-situ data
Tables of water quality parameters vs plume types
Cross-validate with in-situ data
Plots showing cross validation results
Ancillary Data
NERRS Sensors, IBWC River Gage, SD Public Utilities
Delineation of plume extent
Acquiring Data
Visualization
Processing
Outputs
Find plume dates
Plume Delineation
0 5 10 15 20 25
Measurement Comparisons: Remotely-sensed data vs. in-situ data
0 0.5 1.0 1.5
0 1 2 3 4
0 100 200 300 400
0 0.5 1 2
0 0.5 1 2
y = 0.804x + 1.64
R2 = 0.097, n = 28
Remotely-sensed CDOM (m-1)
In-situ CDOM (m-1)
0 1 2 3 5
0 15 30
Kilometers
Kilometers