## Slide 1
Higher suitability for solar development was found in southern regions of the state and areas in proximity to transmission lines.
A majority of the existing solar farms in the counties showed areas of high potential for solar development and low environmental sensitivity.
According to the analysis, Decatur county showed more suitable sites for solar farm development than Taylor county.
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Identifying Suitable Areas for Solar Power Generating Facilities while Reducing Conflicts with Sensitive Habitats
and Wildlife Populations
Solar energy is a rapidly growing industry in the state of Georgia. The increasing popularity of solar farms has encouraged decision-makers and developers to incorporate a sustainable plan for utility-scale solar developments. However, the construction and siting of solar farms could have a threatening impact on environmentally sensitive habitats and associated species. NASA DEVELOP partnered with The Nature Conservancy and the Georgia Department of Natural Resources to conduct an analysis to inform solar site planning and to communicate with key stakeholders. The team analyzed land cover trends from Landsat 8 Operational Land Imager (OLI), in addition to solar insolation data sets from Terra’s Clouds and the Earth’s Radiant Energy Systems (CERES) sensor. These Earth observations were combined to classify and extract data layers for a solar site suitability and conflict identification model following the Land Use Conflict Identification Strategy (LUCIS). Additionally, the DEVELOP team utilized habitat layers of the endangered gopher tortoise (Gopherus polyphemus) primarily due to its role as a keystone species in these sensitive areas. These data were used to generate end products that depict potential conflicts between ideal solar energy sites and endangered species habitats, and prioritize development areas outside of these conflicts. The team examined potential conflicts in Decatur and Taylor counties with additional datasets on existing solar utility infrastructure and parcel data to provide a local-level analysis. The results of this project will be utilized by The Nature Conservancy and Georgia Department of Natural Resources to recommend suitable sites for environmentally conscious solar farm construction.
Georgia Energy II
Georgia – Athens
Fall 2017
Suravi Shrestha
Project Lead
Fabiola
Clermont
Marie
Bouffard
Peter
Hawman
Austin
Stone
Amanda
Aragon
Emad
Ahmed
Nick
Morgan
Caren
Remillard
Develop Goals, Objectives, and Criteria for Land-Use Conflict Identification Strategy (LUCIS) Model
Stakeholder Needs: Environmental and Solar Developer
Environmental Sensitivity
Acquire and Input Data into Land-Use Scenarios
Solar Development Potential
Product: Suitability Map for Solar Development Potential
Product: Map Indicating Environmentally Sensitive Areas
Transmission Lines (TNC)
Slope
(DEM)
Solar Insolation (CERES)
Aspect
(DEM)
Land-Use (CropScape)
Roads
(GA)
Parcels
(GA)
Gopher Tortoise Habitat (UGA)
Protected Lands (GADNR)
Granite Rock Outcrops (NRCS)
Floodplains
(FEMA)
Prime Farmland
(NRCS)
Streams
(NWI)
Land-Use (CropScape)
Product: Bivariate Map
Product: Suitability Map
Platform | Instrument | 
Terra (1999) | Clouds and the Earth’s Radiant Energy System (CERES) | 
Landsat 8 (2013) | Operational Land Imager/Thermal Infrared Sensor (OLI/TRIS) | 
The Nature Conservancy
Georgia Department of Natural Resources
Solar Farm
Development Potential
Environmental Sensitivity
Protected Areas
Low Suitability
Moderate Suitability
High Suitability
Counties
Environmental Sensitivity
Solar Suitability Map
Bivariate Map
Taylor
County
Decatur
County
Georgia
Conduct in-depth solar site suitability analysis on Decatur and Taylor counties
Analyze land cover change in selected counties with regards to solar development
Integrate data on environmental sensitivity and infrastructural site suitability to map ideal locations for utility-scale solar development within Georgia
Provide decision-makers with tools to assist in selecting solar development sites
We would like to thank our science advisor, Dr. Marguerite Madden, for her advice and guidance throughout this project, as well as our past contributors Lynn Abdouni, Natalia Bhattacharjee, Roger Bledsoe, Christopher Cameron.
We would also like to thank our partners Cassidy Jordan and Mat Elliot for their support and involvement throughout the project as well as Sara Gottlieb, Dr. Paul Stackhouse, and Dr. Jeff Hepinstall-Cymerman for their assistance.