## Slide 1
Southwest US Disasters
Jason Zylberman (Project Lead)
Jennifer Holder
Lance Watkins
Incorporating CDRs and MODIS to Create a Predictive Model of Post-Burnout Vegetation Regrowth in Relation to Flood Risk

## Slide 2
Record post-wildfire vegetation response
Identify post-wildfire precipitation thresholds
Establish spatio-temporal relationship between vegetation and precipitation
Objectives
Image Credit: USGS
Introduction Data Methods Results Limitations Future Work Conclusions
1
2
3
Notes: Image Source: http://pubs.usgs.gov/of/2008/1274/images/coverphoto.jpg

## Slide 3
Wildfires and flooding cause economic damage and loss of life in the Southwest
Flood events lead to increased soil erosion and larger debris
Community Concerns
Image Credits: US Forest Services
“Remote Sensing capabilities are an important tool for situational awareness to understand extent of wildfires in both the wildland urban interface and remote and rugged terrains.”
- USGS Southwest Region Wildfire Science Plan, p1
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: http://www.fs.fed.us/managing-land/fire

## Slide 4
Study Area
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 5
PERSIANN - Precipitation Estimation From Remote Sensing Information Using Artificial Neural Network
Specifications:
  0.25 deg * 0.25 deg
  Daily Product
NOAA Climate Data Records
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: Derived from PERSIANN data in ArcMap

## Slide 6
MODIS NDVI: Moderate Resolution Imaging Spectroradiometer Normalized Difference Vegetation Index
Consistent spatial and temporal comparisons of vegetation conditions
Terra MODIS NDVI
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: Derived from MODIS NDVI data in ArcMap

## Slide 7
USDA Forest Service Burned Area Emergency Response (BAER) Imagery Support
Burn severity product called the Burned Area Reflectance Classification (BARC)
differenced Normalized Burn Ratio (dNBR)
BAER Data
Image Credit: BAER Team
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: http://activefiremaps.fs.fed.us/baer/download/2002/rodeo_20020824_postfire_quicklook.jpg

## Slide 8
NOAA Storm Events Database
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 9
Spatial Methodology
MODIS NDVI
BARC burn severity maps
Calculate monthly average NDVI for burned areas
PERSIANN precipitation
Aggregate data to monthly sums
Associate flood records to fire events
Convert floods in study area to raster format
Identify relationships using a multivariate statistical regression
Calculate normals and anomalies
Resample rasters to common resolution
Resample rasters to common resolution
*Process was repeated for all three basins – Salt, Santa Cruz, and Little Colorado
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Pre-process satellite records (PERSIANN and MODIS), identify spatial extent, aggregate to temporal scale, run analysis

## Slide 10
Tabular Methodology
Generate raster statistics for monthly data
Generate raster statistics for raw data and anomalies
Associate flood records to fire events
Align NDVI, flood, and precipitation data to identify trends across variables each year after a wildfire
Calculate daily and monthly normals and anomalies for historical floods
Calculate monthly average NDVI for burned areas
Average daily values for each summer month
Use flood dates to determine
precipitation
*Tabular statistics were combined for all three basins
MODIS NDVI
BARC burn severity maps
PERSIANN precipitation
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Pre-process satellite records (PERSIANN and MODIS), identify spatial extent, aggregate to temporal scale, average spatial statistics to get a single summary statisitc, run analysis

## Slide 11
Data Alignment
MODIS NDVI and PERSIANN precipitation data, 2001-2014
Animation created in GRASS GIS
Animation Credit: Jennifer Holder
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Demonstrate how data was aligned

## Slide 12
Precipitation anomalies, average NDVI, fire events, and flood events were combined for each of the three study basins
Basin Statistics
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 13
Generalized Linear Models (left) and Classification Trees (right) were calculated for each basin
Basin Statistics
Introduction Data Methods Results Limitations Future Work Conclusions
Flood Event ~ Precipitation Anomaly + Average NDVI |  |  |  | 
 | Coefficient | Std. Error | Z-value | Pr(>¦z¦)
(Intercept) | 0.46966 | 1.88487 | 0.249 | 0.8032
Precipitation Anomaly | -0.02583 | 0.01173 | -2.202 | 0.0277 (0.01 significant )
Average NDVI | 1.93816 | 3.55814 | 0.545 | 0.5860
Little Colorado Basin
Negative precipitation anomalies correlate to post-fire floods

## Slide 14
NDVI Trends
Animation of NDVI Regrowth for Rodeo-Chediski Fire, 2001-2014
created in GRASS GIS
Animation Credit: Jennifer Holder
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: More specifically looking at NDVI regrowth

## Slide 15
NDVI Trends
Vegetation response was calculated monthly for historical wildfire events
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 16
Linear Trends
In general, a positive correlation is present between post-fire vegetation response and related flooding incidents
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 17
Flood Data:
  Need more consistent, longer flood record indicating flood magnitude
  Current ground network is sparse
  Flood product from satellite records could be useful (future CDR)
Burn Data:
  Inconsistent quality and completeness
Data Limitations
Image Credit: Kevin Dooley
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: https://www.flickr.com/photos/pagedooley/3992185515

## Slide 18
Limitations
Image Credit: Apache-Sitgreaves National Forest
Methodology:
  Better identify which floods are linked to burned areas
  Resampling data to common formats reduces detail
  Aggregating data eliminates spatial and temporal factors
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: https://www.flickr.com/photos/apachesitgreavesnf/5967273538/in/photolist-a6iQww-a6fZ3p-a6rKRa-a6rmLF-a6fVAx-a6iLZL-a6reVn-a6qFH8-a6fVvP-a6phvM-a6sdc6-6ufSim-9EWhJV-hxTB8U-e3ssQT-nQfvLt-9SL2T4-acSJSH-edDHmJ-ahY71V-acVxoU-6TZVJ3-9pGaQy-btQFBW-bsmW6C-7cCASW-9pLqR4-ownMPc-9pGaTL-3mRJZ6-a2Q3H-3mWbrs-6gEqRS-cYsJAA-bwPYke-bwPYpK-5dVYDo-24pqAv-cFqcvJ-9Mxjph-e18KQx-dbWsLy-awvWae-2Xz1NL-2Xuy3x-2XuA88-2XyQb3-2Xuuza-2XuEsZ-2Xz5vq

## Slide 19
Improve flood inputs:
Potential flood data alternatives
Identify flood extent via satellite brightness pixel values
Creation of a NOAA Flood CDR
Future Work
Image Credit: NRT Global Flood Mapping
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 20
Future Work
Refine Methodology:
Examine change in modeled flood hazard during regrowth
Establish easier access to useful flood data (i.e. NASA DEVELOP Python Module)
Study a different area with better flood records
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 21
More precipitation is needed to initiate post-wildfire floods as vegetation recovers
Trends are observable in the field, but complicated to capture across space and time
Satellite data provides a regional picture in areas with limited in situ data
Conclusions
Image Credit: Ken Bosma
Introduction Data Methods Results Limitations Future Work Conclusions
Notes: Image Source: https://www.flickr.com/photos/kretyen/14367691482/

## Slide 22
NASA DEVELOP National Program
ArcGIS Online Web Map
More Information:
Introduction Data Methods Results Limitations Future Work Conclusions

## Slide 23
Dr. DeWayne Cecil, NOAA National Centers for Environmental Information
Dr. Gregg Garfin, Climate Assessment for the Southwest
Tim Brown, Western Regional Climate Center
Dennis Staley, USGS Landslides Hazards Team
Jason Kean, USGS Landslides Hazards Team
Michael Schaffner, NWS
Christopher Smith, USGS
Advisors
Partners
Others