## Slide 1
500 km
250
125
0
Crea Creek
Canvasback Lake
Goldstream Valley
Area 1002
Bear Lake
Selawik
SAR’s sensitivity to water and reliable data collection on cloudy days make it a valuable source of data for mapping inundation in Alaska.
Landsat 8 OLI and Planet Imagery were limited by cloud cover and detection of inundation below canopy cover, but were helpful for validating Sentinel-1 C-SAR classifications.
This algorithm allows for the efficient production of inundation maps in Alaska that can supplement current wetland mapping efforts.
Modeling site
Abstract
Objectives
Study Area
Earth Observations
Bruce Chapman, NASA Jet Propulsion Laboratory
Megan Lang, US FWS, National Wetlands Inventory
Jeremy Nicoll, Alaska Satellite Facility
Franz Meyer, Alaska Satellite Facility
This material contains modified Copernicus Sentinel data (2017), processed by ESA.
Acknowledgements
Conclusions
Alaska’s wetlands cover approximately one third of the state and provide a multitude of ecosystem services, including nutrient retention, water purification, and provision of habitat for fish, wildlife, and vegetation. The temporal variation in wetland inundation affects these ecosystem functions, and for effective wetland policy and management, it is important to track patterns and changes in inundation. In collaboration with the US Fish and Wildlife Service (USFWS) and the Alaska Satellite Facility (ASF), the fall 2018 NASA DEVELOP Alaska Ecological Forecasting team produced an inundation tool to detect and classify inundation extent in Alaska’s wetlands from C-band synthetic aperture radar (C-SAR) data. The team used Earth observation products, including Sentinel-1 C-SAR, Landsat 8 Operational Land Imager (OLI), PlanetScope, and RapidEye satellite imagery, to create the tool’s thresholding algorithm and generate land cover classifications for validation. The inundation tool effectively mapped wetland inundation due to SAR imagery’s sensitivity to water and reliable data collection on cloudy days. The optical datasets, Landsat 8 OLI and high resolution Planet imagery, were limited by cloud cover and detection of inundation below vegetation and canopy cover but were helpful for visual validations of Sentinel-1 C-SAR classifications. The tool’s ability to map wetland inundation can support the development and refinement of National Wetland Inventory (NWI) wetland maps in Alaska and build the capacity of operational federal programs to use SAR.
California – JPL | Fall 2018
Alaska Ecological Forecasting
Automated Wetland Hydroperiod Mapping by Integrating Optical Satellite Imagery and Synthetic Aperture Radar
Create algorithm to detect wetland inundation extent from Sentinel-1 C-band SAR data
Validate algorithm using optical imagery
Integrate algorithm with the Alaska Satellite Facility SAR processing tool, HyP3
Enhance the National Wetland Inventory’s mapping capability through inundation map generation
Landsat 8 OLI
PlanetScope & RapidEye
Sentinel-1 C-SAR
Figure 1: Inundation extent or areas open water and inundated vegetation (in white) derived from Sentinel-1 C-SAR data.
Methodology
US Fish and Wildlife Service, National Wetlands Inventory
Alaska Satellite Facility
Project Partners
Input
Processing
Calibration
Classification
Validation
Output
Sentinel - 1
C-SAR
VV VH
Landsat 8 OLI
PlanetScope
Optical
Data
UTM Projection
Image Coregistration
Subset
Multi-Temporal
Average
Multi-Temporal
Mean Ratio
VV / VH
Ratio
Average Region
Brightness
Average Pixel
Brightness
Normalize
VV, VH,
VV/VH
Thresholds
Classification
Per Date
Multi-Temp
Classification
Refined
Classification
Accuracy
Assessment
Landcover
Classification
Wetland Inundation Map
Landcover
Classification
Team Members
Figure 2: Dynamic Surface Water Extent model output on Landsat 8 OLI. Areas in white are classified as inundated.
Figure 3: Normalized difference water index for PlanetScope image. Brighter areas indicate higher NDWI values.
Bear Lake: Mapping Temporal Fluctuations in Inundation
Single Date Classifications
Bear Lake: Typical Inundation State
Multi-Temporal Averages from June 2017 to September 2017
Open water
Not inundated
Inundated
Unclassified
Adam Vaccaro
Alice Lin
Annemarie Peacock
Project Lead
Briant Fabela
Figure 4: Multi-temporal averages of VV, VH, and VV/ VH polarizations. Brighter areas indicate higher backscatter.
Modeling site
NWI Project
NWI Project
Main algorithm testing site
Potential NISAR cal/val site
Figure 5: Classification of multi-temporal averages using VV, VH, and VV/VH brightness thresholds.
VV Polarization
VH Polarization
VV / VH Ratio Polarization
July 7, 2017
July 6, 2017
July 7, 2017
0 2.5 5 10 km
Results