## Slide 1
Abstract
Objectives
Methodology
Study Area
Results
As a largely snowmelt-fed watershed, Utah’s Fremont River Basin provides year-round irrigation for approximately 16,000 acres of agricultural areas, including historic orchards and pastures maintained by Capitol Reef National Park (CARE). However, forecasts for seasonal water availability within the basin based on in situ snowpack data have been unreliable compared to water use allocations in the past. For this reason, a more robust method was required to provide accurate water availability assessments that help CARE plan future water allocations more effectively. Multiple NASA Earth observations and in situ data were employed to derive key trends and data insights for snowmelt and relevant climate variables across the watershed. Furthermore, a forecasting tool that predicts seasonal streamflow in the Fremont River Basin was created using machine learning models. The results of the snowmelt and climate analyses along with the forecasting tool will inform water resource management and enhance future irrigation allocation plans at CARE.
Virginia – Wise | Summer 2018
Fremont River Basin Water Resources II
Water Availability Assessment from Annual Snow Cover in the Fremont River Basin Based on NASA Earth Observations and In Situ Data
Conclusions
In situ and remotely sensed Terra MODIS data are effective inputs for training machine learning algorithms to forecast streamflow.
SPAM exhibited greater accuracy (MAE, RMSE) in modeling streamflow over SNOW-M.
The Streamflow variable was most correlated with Precipitation and Snow Cover Area.
Mean Snow Cover Area data greatly fluctuated year to year from 2000 to 2017, with 203.15 sq. km in 2001 (min. year) and 399.44 sq. km in 2009 (max. year)
Devise the most suitable model to forecast streamflow in the Fremont River Basin
Conduct an Exploratory Data Analysis report revealing key snowmelt and climate trends over time
Visualize time series of snow cover changes in the Fremont River Basin
EXAMPLE
Earth Observations
Terra MODIS
Landsat 5 TM
Team Members
Jessica Li
Project Lead
Zhuoyan He
Chenyu Shi
ArcSWAT Watershed Delineation
In-situ SNOTEL Data
DEM
Predicted Streamflow
MODIS NDSI
Snow cover Maps
MODIS
LST
PERSIANN Precipitation
In-situ Stream Gauge Data
Elevation Zones
SPAM
Confidence Intervals
GUI Tool
Additional Variables
SNOW-M
Comparison
Exploratory Data Analysis
UT
NV
AZ
NM
CO
WY
ID
Stream gauge
SnoTEL station
River
Fremont River Basin
Low Elevation Zone
Moderate Elevation Zone
High Elevation Zone
Capitol Reef National Park
Fremont
Lyman
Bicknell
Torrey
Teasdale
Acknowledgements
Joseph Spruce, Lead Science Advisor for NASA DEVELOP VA – Wise County
Dr. L. DeWayne Cecil, Chief Climatologist at NOAA National Centers for Environmental Information and Program Manager of Global Science & Technology, Inc.
Bob VanGundy, Geology Instructor at The University of Virginia’s College at Wise
Brooke Colley, Center Lead at NASA DEVELOP Wise County Clerk of Circuit Court’s Office
Margaret Mulhern, Manda Au, Nolan Barrette, & Austin Counts, NASA DEVELOP VA – Wise County
Actual
Predicted
Actual vs. Predicted Streamflow by SPAM
Streamflow (m3/s)
Day since September 14, 2011
Project Partners
Capitol Reef National Park
National Park Service, Northern Colorado Plateau Network
Actual vs. Predicted Streamflow by SNOW-M
Actual
Predicted
2016-2017 Water Year
Streamflow (m3/s)
Area(sq. miles)
Difference
Snow Cover Area for Minimum and Maximum Years vs. Mean Snow Cover Area
Snow Cover
0
30
60
15
Kilometers
Mean Snow Cover Area (2000-2016)
Annual Snow Cover Area in 2000-2016
2001 (Minimum)
2009 (Maximum)
River
Basin
CARE
River
Basin
CARE
0 - 1 %
1 – 1.5 %
1.5 – 2.5 %
2.5 – 4.5 %
4.5 – 9 %
9 – 17 %
17 – 34 %
34 – 68 %
-100 - -70 %
-70 – -40 %
-40 – 0 %
0 – 150 %
150 – 250 %
250 – 350 %
350 – 550 %
550 – 750 %
750 – 1,750 %
150
140
130
120
110
100
90
80
2000
2002
2004
2006
2008
2010
2012
2014
2016
6
5
4
3
2
1
50
100
150
200
250
300
350
6
5
4
3
2
1
500
0
1000
1500
2000