## Slide 1
Utilizing NASA Earth Observations to Assess Agricultural Drought Severity in Ethiopia and Provide a Tool for Monitoring Drought at the Regional Level
ETHIOPIA DISASTERS
Amandeep Vashisht (Team Lead)
We would like to thank Dr. Paul Evangelista, Dr. Amanda West, Ryan Anderson, and Brian Woodward of Colorado State University.
This material is based upon work supported by NASA through contract NNL11AA00B and cooperative agreement NNX14AB60A. Any mention of a commercial product, service, or
activity in this material does not constitute NASA endorsement. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily
reflect the views of the National Aeronautics and Space Administration and partner organizations.
.
Ethiopia has recently been affected by several droughts, with the latest 2015 drought being the worst in half a century. Agriculture, being the predominant sector of the country’s economy, is rain-fed and is therefore most susceptible to droughts. Developing a reliable remotely sensed tool that incorporates a combination of drought-related parameters can help in better detection of drought events with respect to their spatiotemporal extent, duration and severity. This project implemented a scaled drought index utilizing NASA’s Terra Moderate Resolution Imaging Spectroradiometer (MODIS), Tropical Rainfall Measuring Mission (TRMM) and Global Precipitation Measurement (GPM) Integrated Multi-satellite Retrievals for GPM (IMERG) data to assess drought at a regional scale over the last 10 years. The index maps and decision support tools were provided to the project partners to supply timely information for humanitarian aid, and to build their capacity to monitor droughts in the future.
Develop a scaled drought index to characterize drought conditions
Analyze drought severity and spatiotemporal variation across the study area
Create tutorials for partner organizations to build their capacity to monitor drought in the future
Abstract
Objectives
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Sarah Carroll
Rebecca Girma
USGS at Colorado State University – Fall 2016
Data Acquisition
  Vegetation index and land temperature from MODIS
  Rainfall from TRMM
  Soil moisture from SMAP
Data Processing
  Resample data
  Aggregate to monthly values
  Scale values
  Weight drought parameters
  Combine parameters
Data
Analysis
  Create drought index
  Analyze spatial variation across climate zones
  Compare results to soil moisture trends
Bethlehem Astella
Cara Steger
Study Area
Methodology
Terra Moderate Resolution
Imaging Spectroradiometer
(Terra MODIS)
Aqua Moderate Resolution Imaging Spectroradiometer
( Aqua MODIS)
Tropical Rainfall
Measuring Mission
(TRMM)
Soil Moisture Active Passive
(SMAP)
US Department of State Office of Space and Advanced Technology (OES/SAT) and Humanitarian Information Unit (HIU)
Institute of Geo-Information and Earth Observation Sciences (I-GEOS)
USGS North Central Climate Science Center
Chart: Year
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Area Under Severe Drought (sq. km) | 3 | 1267 | 142 | 23037 | 535 | 6040 | 3415 | 272 | 207 | 31435
Drought Index Time Series Across Climatic Zones
2007
2006
2008
2009
2010
2011
2012
2013
2014
2015
I
II
IV
III
Climatic Zones:
I. North West Highlands
II. North East Highlands
III. South West Rainforest
IV. Central Highlands
Drought Index
High: 1 (wettest)
Low: 0 (driest)
Addis Ababa
Dese
Debre Birhan
Finote Selam
Debre Mark’os
Bahir Dar
2015 Drought Classification Map
Extreme drought
Severe drought
Moderate drought
Abnormally dry
No drought
Cities
Study Area Boundary
Ethiopia Boundary
Regional Boundary
ETHIOPIA
Kenya
Somalia
Yemen
Addis Ababa
Benishangul -
Gumuz
Oromia
Amhara
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
Scaled Drought Index | 0.22105 | 0.26416 | 0.10349 | 0.098371 | 0.64917 | 0.70002 | 0.68113 | 0.64179 | 0.34083 | 0.40204 | 0.37333 | 0.35713 | 0.27019 | 0.33533 | 0.23026 | 0.084755 | 0.33736 | 0.31732 | 0.24217 | 0.11229 | 0.70912 | 0.59863 | 0.21991 | 0.30189 | 0.45328 | 0.33012 | 0.13961 | 0.11646 | 0.74935 | 0.68406 | 0.37497 | 0.2978 | 0.71681 | 0.57217 | 0.2879 | 0.25274
Scaled SMAP surface soil moisture | 0.23805 | 0.19005 | 0.17232 | 0.036591 | 0.32275 | 0.39613 | 0.32991 | 0.16111 | 0.42784 | 0.48758 | 0.33193 | 0.15231 | 0.52075 | 0.59192 | 0.4498 | 0.14802 | 0.67066 | 0.69201 | 0.61735 | 0.31198 | 0.68935 | 0.72941 | 0.65781 | 0.37412 | 0.59316 | 0.65877 | 0.55814 | 0.211 | 0.60121 | 0.63284 | 0.52417 | 0.17411 | 0.54665 | 0.53559 | 0.48468 | 0.14912
Drought Index and Soil Moisture Comparison
Nov
Area Under Extreme - Severe Drought
total area: 120,000 km2
June
July
Aug
Sep
Oct
North-West Highlands
South-West Rainforest
Central Highlands
North-East Highlands
The drought index captured the severity and extent of drought from 2006-2015 across the study area.
In 2009 the NW Highlands and SW Rainforest experienced severe drought whereas in 2015 the NW Highlands and central Highlands experienced severe drought.
The drought index and SMAP soil moisture values showed similar trends for the 2015 growing season.