## Slide 1
NASA Jet Propulsion Laboratory
Validating Satellite Observations of Wastewater Plume Biological Impacts in Santa Monica Bay, California
Los Angeles Oceans II
Lindsay Almaleh and Rebecca Trinh
Hyperion Water Reclamation Plant,
City Of Los Angeles
Science advisors: Ben Holt and Michelle Gierach, NASA JPL
Project partners: Curtis Cash, Ashley Booth, and Mas Dojiri, Hyperion Water Reclamation Plant
Cedric Fichot, NASA JPL
Jayme Smith, USC
Carter Ohlmann, UCSB
NASA DEVELOP National Program
Previous Contributors: Mark Barker, Christine Rains, and Jack Pan
Coordinate with the Hyperion Water Reclamation Plant research team in obtaining in situ data taken in the Santa Monica Bay.
Validate NASA Earth observations and in situ data taken during the diversion event.
Determine whether the expelled effluent has negatively impacted the local ecosystem or washed ashore to potentially contaminate beaches.
Publish results in a journal and Hyperion’s technical report.
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Rebecca Trinh (Project Lead), Lindsay Almaleh
DEVELOP National Program at NASA Jet Propulsion Laboratory
Landsat-8
Aqua, MODIS
Terra, ASTER
Study Period: August 31 – November 20, 2015
The Hyperion Water Reclamation Plant is one of the largest wastewater treatment plants in the western United States. Treated sewage is generally released at depths of approximately 60 m through 8.05 km outfall pipes into a deep marine canyon in the Santa Monica Bay. In times of repair and maintenance, services on the main outfall pipe are temporarily suspended and require the plant to divert treated sewage to a shorter 1.6 km pipe that extends into shallow coastal zones. These shallow zones make it possible for the buoyant freshwater plumes to reach the surface, potentially contaminating the local environment. A six-week diversion event occurred at HWRP from September 21 to November 2, 2015. This project plans to integrate previously obtained NASA satellite images and ancillary data collected by other scientists. By combining remotely-sensed observations with GPS-equipped drogue surface drifters and in situ readings of temperature, salinity, atmospheric aerosols, and chlorophyll-a florescence, an accurate assessment of the full impact and extent at which these effluent plumes affected the Los Angeles Basin is possible. The outcome of this study can aid in developing proper methods to avoid harmful outcomes during similar diversion events in the future.
Hyperion
Treatment
Plant
LAX
Santa Monica
Bay
Suomi NPP, VIIRS
In situ Atmospheric Aerosol Thickness can be used to atmospherically correct satellite images.
Freshwater and cold sea surface temperature signatures from the effluent are validated via temperature and salinity from Conductivity, Temperature, Depth instrument (CTD).
Algal blooms seen on remote sensed images are validated by in situ chlorophyll-a data from CTD and water chemistry.
Obtaining data using multiple methods can help validate all measurements.
BEFORE
ASTER
AFTER
MODIS
Atmospheric Correction
BEFORE
AFTER
CTD
In Situ Comparison
Temperature
Landsat-8
Oct. 10, 2015
Drifter
Direction
Extrapolated Aerosol Optical Thickness (AOT)
Wavelength (nm)
AOT
Chlorophyll-a
surface sediment
turbidity
Sea surface temperature
In Situ Measurements
NASA Earth Observations:
Spatiotemporal
analysis of combined
datasets
Terra, ASTER
Salinity, temperature, chlorophyll-a
Local current direction
Algal blooms
Suomi NPP, VIIRS
Aqua, MODIS
Landsat-8, OLI/TIRS
Atmospheric correction
Microtops, JPL
Atmospheric aerosols
Phytoplankton,USC
CTD, HWRP/UCSB
Drifters, USCB