## Slide 1
Great Lakes Water Resources
Objectives
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Improving Wetland Change Mapping using Optical and Radar Satellite Sensors to Assess Wetland Gain and Loss Metrics in Minnesota
California – JPL | Spring 2019
Wetlands are a critical feature of our landscape for the ecological services they provide, including protecting water quality, providing habitat to rare species, mitigating erosion, and providing opportunities for recreation. Despite this, wetlands are facing increasing threats from a variety of anthropogenic sources, including pollution, change in climate, and commercial development. Although an accurate baseline inventory of wetland extent is essential for addressing these threats and quantifying future wetland change, traditional wetland mapping methods are time intensive, costly, and difficult to implement on a large scale. Here we show that statewide, fully-automated wetland mapping is possible to a high degree of accuracy by combining recent advances in remote sensing and cloud computing. Using a multi-source, multi-temporal, object-based random forest classification approach in Google Earth Engine, we generated 30 m resolution maps of wetland extent and change for the growing seasons (May through September) of 2017 and 2018 in Minnesota. In particular, inclusion of Sentinel-1 C-Band Synthetic Aperture Radar (C-SAR) composites, Landsat 8 Operational Land Imager (OLI) composites, and a topographically derived wetness index allowed us to achieve and overall accuracy of 87% when compared to the National Wetland Inventory. Our partners included US Fish and Wildlife Service (USFWS) National Wetlands Inventory (NWI), Minnesota Department of Natural Resources (MN DNR), Environmental Protection Agency (EPA), Ducks Unlimited (DU), National Oceanic and Atmospheric Administration (NOAA) Office for Coastal Management, and the University of Minnesota (UMN). We anticipate that our tool can be of immediate use to these end users in Minnesota who rely on accurate wetland data to inform their research, policy, and development decisions. Furthermore, these methods can quickly be applied to any region of the United States for which adequate training data exists.
Abstract
An overall classification accuracy of 87% was achieved, when comparing the Random Forest classification to the field data points.
The Random Forest classification map validated against the field points was the most accurate result.
Additional field validation points, particularly in the open water class, are needed.
Further work can be done to investigate how accuracy changes with the inclusion of additional datasets (soil, Sentinel-2) and classification methods (pixel vs. object).
Erika Higa, DEVELOP California – JPL Node (Center Lead), Neda Kasraee, DEVELOP California – JPL Node (Impact Analysis Fellow & Assistant Center Lead), Bruce Chapman, NASA Jet Propulsion Laboratory, California Institute of Technology (Science Advisor), Benjamin Holt, NASA Jet Propulsion Laboratory, California Institute of Technology (Science Advisor), Brian Huberty, US Fish and Wildlife Service National Wetland Inventory (US FWS NWI), Steve Kloiber, Minnesota Department of Natural Resources (MN DNR), Tom Hollenhorst, Environmental Protection Agency (EPA), Robb Macleod, Ducks Unlimited (DU), Joe Knight, University of Minnesota (UMN), Brandon Krumwiede, NOAA
This material contains modified Copernicus Sentinel data (2017-2018), processed by ESA.
Improve wetland change mapping using radar and optical datasets, including NASA Earth observations, to aid end users in assessing wetland gain and loss in Minnesota
Create an automated, multi-satellite, and seasonal approach for wetland mapping that can efficiently account for changes in wetland extent
Build our end users’ capacities to utilize radar data and the cloud computing abilities of Google Earth Engine for wetland mapping
US Fish and Wildlife Service, National Wetland Inventory
Minnesota Department of Natural Resources
US Environmental Protection Agency, Office of Research and Development
Ducks Unlimited
University of Minnesota
NOAA Office for Coastal Management
Landsat 8 OLI
Sentinel-1 C-SAR
0 30 60 120 180 240
km
Christopher Notto
Alice Lin
Erica O’Connor
Project Lead
Melissa Ferriter
Fond Du Lac Reservation:
2017 Growing Season
Minneapolis
Fond Du Lac Reservation:
2017 Growing Season
2018 Growing Season
0
2
4 km
0 5 10 15 km
M I N N E S O T A
U N I T E D
S T A T E S
3,000 km
2,000
1,000
0
Random Forest Classification:
2017 Growing Season
Upland
Open Water
Wetland
0 500 1000 km
Methodology: Wetland Extent Tool (WET)
Filtering
Pre-Processing
Classification
Validation
Change Detection
Landsat 8 OLI
MN State
Date
Cloud Cover
Sentinel-1 C-SAR
MN State
Date
IW Swath
Border Removal
Convert To Natural Values
Mean Composite
(Resampled to 30 m)
LiDAR Derived TWI
(Resampled to 30 m)
Image Stack
TCWGD, MNDWI
Mean composite
VV,VH
SNIC Image Segmentation
Specified Thresholds
Random Forest Classification
Preliminary Classified Wetland Map
Accuracy Assessment
2017 Wetland Map
2018 Wetland Map
Confusion Matrix
Change Detection Map
Cloud Mask
Field data