## Slide 1
Central Valley Water Resources
California - JPL
Improving California Groundwater Assessments using
GRACE and InSAR Datasets for Water Resource Management
Abstract
Evaluate groundwater storage
Evaluate surface elevation subsidence
Characterize temporal relationship of groundwater & subsidence
Characterize spatial relationship of groundwater & subsidence
Assess groundwater & subsidence change within each sub-basin
Objectives
Methodology
Central Valley, California, USA
Area: 20,000 square miles
Population: 6.5 million (2018)
California: 11% of the state’s total land area, supplies 60-75% of the state’s water
Agriculture: Produces ~50% of United State’s nuts, fruits, and vegetables within 17% of total U.S. irrigated land
Concerns: Currently the rate of groundwater pumping is unknown, and in some areas land is sinking at a rate of more than 18 inches a year
Study Area
Seasonal minima and maxima, in addition to periods of drought, can be detected and readily correlated across in-situ (well and GPS) and remotely sensed (InSAR and GRACE) analysis methods.
Sub-basin scale snapshots provide locally-relevant information as a basis for decision-making for land managers.
GRACE and InSAR data can be relied on to provide groundwater storage and subsidence data in regions with sparse in-situ well and GPS data.
Conclusions
We would like thank our science advisors at the NASA Jet Propulsion Laboratory (JPL) for their guidance during this term and for providing the Earth observation data required for this study: Dr. Zhen Liu, Dr. Kyra Kim, and Dr. John T. Reager. We also thank JPL’s Benjamin Holt and NASA DEVELOP Fellow Cecil Byles for their support throughout this study.
This material contains modified Copernicus Sentinel data (2015-2020), processed by ESA.
Acknowledgements
California Department of Water Resources, North Central Region, South Central, & Southern Region Offices
California State University, Los Angeles
Project Partners
Team Members
California’s Central Valley is one of the most productive agricultural areas in the world, producing approximately $20 billion in crops annually. The recent California droughts of 2007-2010 and 2012-2019 resulted in increased groundwater pumping in the Central Valley to adequately irrigate farmland. Overdrafting of the Central Valley aquifer results in groundwater depletion, land subsidence, and permanent loss of groundwater storage. In 2014, depletion of groundwater led the state of California to enact the Sustainable Groundwater Management Act (SGMA), requiring critically overdrafted, high, and medium priority sub-basins to reach sustainable levels of groundwater pumping and recharge by 2042. SGMA allows local Groundwater Sustainability Agencies (GSAs) the authority to create Groundwater Sustainability Plans (GSPs) at the sub-basin level. To assist California’s Department of Water Resources (DWR), this project quantified groundwater change and land subsidence in Central Valley sub-basins with sparse or unreliable well and Geographic Positioning Systems (GPS) data. This was done using NASA’s Gravity Recovery and Climate Experiment (GRACE), GRACE Follow On (GRACE-FO), and interferograms derived from Sentinel-1 C-band Synthetic Aperture Radar (C-SAR) and Advanced Land Observing Satellite 2 (ALOS-2) Phased Array L-band Synthetic Aperture Radar 2 (PALSAR-2). Time series of the GRACE and InSAR data were compared with well and GPS data in data-dense sub-basins to determine the feasibility of these datasets for groundwater storage and subsidence monitoring. We found that GRACE and InSAR data are effective tools for determining groundwater change and land subsidence and can be used on their own to monitor sub-basins in the absence of well and GPS data.
Forrest Corcoran
Project Lead
James Kitchens
Patrick Saylor
Marissa Dudek
Results
Zonal Trends:
Delta-Mendota Sub-basin
Count of Well Observations (#)
Well Water Surface Elevation
(Z-Score)
InSAR Ground Surface Elevation
(Z-Score)
GRACE Groundwater Thickness (Z-Score)
Count of GPS Observations (#)
GPS Ground Surface Elevation (Z-Score)
2015 Jan.
2015 July
2016 Jan.
2016 July
2017 Jan.
2017 July
2018 Jan.
2018 July
2019 Jan.
2019 July
3
2
1
0
-1
Drought
2012 - 2016
2004
2006
2008
2010
2012
2014
2016
2018
2020
Z-Score
GRACE
InSAR
WSE
Temporal Trends:
Delta-Mendota Sub-basin
Temporal Analysis: Evaluation of temporal trends from 2003-2019 in the Delta Mendota Sub-basin indicate a distinct decline in groundwater storage during the drought of 2012-2016 as evidenced in InSAR, GRACE, and groundwater well trends. This trend is consistently observed across most sub-basins within the Central Valley.
Groundwater Analysis: The Delta-Mendota sub-basin was selected as a test case to verify the efficacy of this study’s methodology. Zonally averaged time series allow for the comparison of trends in each sub-basin. Delta-Mendota demonstrates a general decreasing trend in well water surface elevation (WSE), that is confirmed by GPS, InSAR, and GRACE observations.
In-Situ and Remote Sensing: Sub-basin Scale Analysis: Data sources were aggregated and evaluated at a sub-basin scale to balance the need for high-resolution interpretations while maintaining broader perspective for land managers. While broad trends exist across the Central Valley, the specific response of each sub-basin to drought conditions and rebound are unique.
In-Situ and Remote Sensing:
GPS, Wells, GRACE, InSar
2003
2020
GRACE
Groundwater Storage
San
Francisco
2015
2019
InSAR Surface Subsidence
San
Francisco
N
N
High
Very High
Medium
Very Low
Sub-basin
Sustainability
Priority
N
Sparse
Dense
GPS
Station
Density
Sparse
Dense
Well
Station
Density
Delta-
Mendota
Sub-basin
GRACE &
GRACE-FO
Earth Observations
Sentinel-1
(C-SAR)
ALOS-2
(PALSAR-2)
N
500
250
0
Kilometers
Central Valley
Sierra Nevada
Mountains
Coast
Ranges
Los Angeles
San
Francisco
CALIFORNIA
Acquire study area in-situ & remotely sensed data
Process raw data
Aggregate in-situ and remote sensing data
Evaluate surface subsidence and groundwater storage change spatially and temporally at the sub-basin scale
In-Situ: Well & GPS
EOs: GRACE/InSAR
Quality control, normalize data
Spatially and temporally
Maps, time-series, rate of change charts