## Slide 1
Utilizing a Landslide Identification Product and a Real-time Rainfall Detection Tool for Enhanced landslide Detection in Nepal
Himalaya Disasters III
Amanda Rumsey, Jessica Fayne, Jordan Scheffler
ICIMOD
Use bullets.
Use complete sentences with periods.
Keep this blank for now.
Body text point size should be at least 24.
Caption text point size should be at least 16.
Feel free to rename, move, and resize sections as needed.
Validate the results of SLIP using digitized landslide event information collected using Landsat 8 imagery
Develop a web-based platform to display the results of the SLIP and DRIP products
Package SLIP and DRIP into a usable program for ICIMOD
Perform rainfall threshold analysis and comparative rain gauge and TRMM analysis for Nepal
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partner
Team Members
Amanda Rumsey (Project Lead), Jordan Scheffler, Jessica Fayne
DEVELOP National Program at NASA Goddard Space Flight Center
GPM
TRMM
IMERG 30-Minute
TMPA-RT 3B42
DRIP
Data Collection
Thresholds
Comparison
SLIP
Landsat 8
SRTM
ASTER
SWIR
IR
Red
QA
Data Collection
Cloud Mask
Red Increase
Moisture Index
Slope Analysis
SLIP and DRIP
Validation
QA band from Landsat 8 is used to remove clouds from the other bands
Calculate percent change between two Red band images
Compare two images’ moisture using IR and SWIR bands
Remove pixels with slopes lower than 15%
SLIP
Landsat 8
Data Comparison
Accuracy Assessment
TRMM
GPM
Landsat 8
Terra
Historical TRMM data was used to calculate monthly mean thresholds used to detect anomalies in near real-time with GPM
Monitors GPM IMERG data every 30 minutes looking for anomalies compared with calculated threshold values
Precipitation monitoring by DRIP
landslide detection by SLIP (Yellow)
Alert!
If current rainfall levels are higher than thresholds, an alert is created
Dr. Dalia Kirschbaum (GSFC)
Thomas Stanley (GSFC)
Sebastian Wesselman (ICIMOD)
Justin Roberts-Pierel (GSFC)
Aakash Ahamed (GSFC)
Jamie Shiplet (Towson University)
Location of Landslide Event | % Accuracy