## Slide 1
International Research Institute for Climate and Society
Applications of flood definitions and NASA Earth Observations to create a flood forecasting methodology
Malawi Disasters II
Andrew Kruczkiewicz, Helen Cen, & Brigitte Moneymaker
Red Cross/Red Crescent Climate Centre: Erin Coughlan
Malawi Red Cross Society: Hastings Kandaya
Dr. Pietro Ceccato
Lead Environmental Monitoring Program, IRI
(Science Advisor)
DFO in Group 2 is better at detecting riverine floods and possibly flash floods as well.
NRT-GFM in Group 2, TerraSAR-X and RADARSAT in Group 1 are good at detecting riverine floods only.
Within the region where flash floods were the only type (Phalombe), soil moisture was elevated at an earlier date and for a longer period of time. Potentially indicating heightened levels of soil moisture and persistence of said heightened levels may drive flash flood risk
The African country of Malawi experiences a strong seasonal rainy season stretching from October to April, which provides approximately 95% of annual precipitation. In addition, approximately 20% of Malawi’s land cover is comprised of surface water from Lake Malawi, one of the Great African Lakes. These unique features contribute to the country’s increased vulnerability to riverine floods and flash floods. In January 2015, extended periods of extreme rainfall caused a series of flood events throughout Malawi, which resulted in the displacement of over 230,000 residents and caused 276 fatalities. In order for local authorities and humanitarian agencies to provide post-disaster relief, these organizations often rely on remotely-sensed satellite data to evaluate initial disaster impact and design response programs. In partnership with the Malawi Red Cross, this project aimed to expand on the findings from previous research in Spring 2015 by first comparing ground-truth data (locations of shelter site of internally displaced people (IDPs) and origins of IDPs) with previous term data and second, by integrating European Space Agency (ESA) remotely sensed data to explore the potential predictive capabilities of soil moisture for flash flood detection. In addition to data from NASA sensors (MODIS, TRMM, SSM-I and AMSU-A data), this project incorporated ASCAT data from ESA. The results of this study will increase the ability to forecast and monitor flood events, benefiting organizations involved with disaster preparedness and relief efforts in Malawi and potentially allowing for more efficient action, including prepositioning of pre-flood resources, response operations and allocation of emergency flood relief efforts.
Use the January 2015 floods in Malawi to compare various inundation detection tools
Validate flood maps with ground truth data provided by the Malawi Red Cross
Explore soil moister detection products in relation to flooding
Abstract
Objectives
Methodology
Study Area
Earth Observations
Results
Conclusions
Acknowledgements
Project Partners
Team Members
Andrew Kruczkiewicz (Project Lead), Helen Cen, Brigitte Moneymaker
NASA DEVELOP National Program at International Research Institute for Climate and Society
Aqua
Terra
TRMM
RADARSAT
RADARSAT-2
TerraSAR-X
DMSP
MetOp-A
MetOp-B
Acquire & Process Ground Truth Data
Group Flood Products
Comparison & Validation
Flood Product
  Group 3: University of Maryland Global Flood Monitoring System Products
  Group 2: Near Real Time Products
  Group 1: SAR Products
RADARSAT
RADARSAT-2
TerraSAR-X
DFO
NRT-GFM
GFMS-FD
GFMS-I
  Group 1
  Group 2
  Group 3
RADARSAT
RADARSAT-2
TerraSAR-X
DFO
NRT-GFM
GFMS-FD
GFMS-I
Flood Product Spatial Analysis
Soil Moisture Product
Flooded Villages Layer
Flood Detection Products
Shelter Sites Layer
Base Layer (Open Street Map)
Soil Moisture Product Analysis
Acquire Data
Selecting Areas of Interest
Zonal Statistical Analysis
Soil Water Index
CMORPH
TRMM
Iso Cluster Unsupervised Classification
Indicates clusters of similar soil moisture characteristics
Soil Water Index
CMORPH
TRMM
IFRC 6 Day Extreme Rainfall Forecast
IFRC 6 Day Extreme Rainfall Forecast
Malawi
Study Period
January 2015
Phalombe Region
Blantyre Region
Shire Region