## Slide 1
N
N
Asheville Urban Development
Abstract
Analyze how land surface temperature and tree cover in Asheville have changed long-term by comparing data from the 1980s to present-day to quantify changes and identify areas that have changed the most
Explore the statistical relationship between tree cover and land surface temperature in Asheville
Identify areas particularly vulnerable to heat in Asheville by generating a heat vulnerability index that incorporates temperature, tree cover, and socioeconomic data
Objectives
Study Area
Earth
Observations
Results
Using NASA Earth Observations to Quantify the Impact of Urban Tree Canopy Cover on Urban Heat and Identify Community Vulnerability in Asheville, North Carolina
North Carolina – NCEI | Fall 2019
Asheville, North Carolina has had a population growth of approximately 10 percent over the past decade, while the city’s tree canopy cover has simultaneously decreased by 6.4 percent. A well-known benefit of urban tree cover is the mitigation of the effects of urban heat islands through factors including shade and evapotranspiration. Thus, as Asheville’s population grows, the presence of trees and their cooling effects is crucial. The Asheville Urban Forestry Commission advises the City Council on issues pertaining to urban development with policies centered on tree cover preservation and growth. The Asheville Urban Development team partnered with the Urban Forestry Commission to complete a study using NASA Earth observations and ancillary datasets to explore relationships between changes in land surface temperature and tree cover over the last 10 years. The team used Landsat 5 Thematic Mapper (TM) and Landsat 8 Operational Land Imager (OLI) to calculate Land Surface Temperature (LST) changes from 1984 to 2018. The team also used socioeconomic data on the census block group level to create a heat vulnerability index in order to identify communities at risk. The team included tree cover and LST data in this index to represent exposure and adaptive capacity as factors in heat vulnerability. The end products illustrated a significant correlation between tree cover and LST in Asheville and identified vulnerable communities to support the Urban Forestry Commission’s decisions about tree planting and preservation.
Landsat 5 TM
Landsat 8 OLI
Methodology
Data Acquisition
Processing
Analysis
End Products
Landsat 5 and 8
Tree cover data
Difference maps
Aggregate variables
Census data
Clip to Asheville
Normalize all
LST change analysis
Linear regression
Scatter plots
Map of heat
vulnerability by
census block group
Derive LST
Calculate means
per block group
Temperature & Tree Cover Analyses
Heat Vulnerability Index
variables
Project Partner
Asheville Urban Forestry Commission
Median LST for warm months has increased by up to 31°F in parts of Asheville over the last 30 years.
The presence of tree cover in Asheville has a cooling effect which can mitigate the urban heat island effect.
Heat vulnerability varies drastically between neighborhoods based on LST, tree cover, age, and poverty.
NASA Earth observations can be used to supplement urban heat vulnerability indices based on US Census data and high resolution tree cover data.
Conclusions
0 2.5 5 10
Median LST 1984 to 1986
N
0 2.5 5 10
Median LST 2017 to 2019
N
Low: 56° F
High: 95° F
LST
Asheville
0 2.5 5 10
Present Day
Tree Cover vs. LST
R² = 0.5374
Y = - 0.1225x + 82.785
Tree Cover Percentage
Land Surface Temperature (ºF)
Chart: 
72
74
76
78
80
82
84
86
20
40
60
80
Highest
Lowest
Heat Vulnerability
Chart: 
 | 0.0054006 | 0.061305 | 0.19077
Lack of
Tree Cover
LST
Social
0.5
1.0
0.0
Asheville School
Chart: 
 | 1 | 0.79404 | 0.86498
Lack of Tree Cover
LST
Social
0.5
1.0
0.0
Downtown
Heat Vulnerability by
Census Block Group
Acknowledgements
Team Members
Darcy Gray
Project Lead
Amy Kennedy
Amiya Kalra
We would like to thank our science advisor Scott Stevens and our fellow Andrew Shannon for their knowledge and guidance throughout this project. We would also like to thank our partners from the Asheville Urban Forestry Commission, including Ed Macie, Dawn Chavez, Stephen Hendricks, Amy Smith, and others. We further recognize representatives from NEMAC, NCEI, the City of Asheville, and others for their assistance in the completion of this project.
35-Year Change in LST for Warm Months
0 2.5 5 10
Kilometers
Kilometers
Kilometers
Kilometers
Chart: 
 | 0 | 0.72 | 0
Lack of Tree Cover
LST
Social
0.5
1.0
0.0
Gorman Bridge
NC
VA
SC
GA