## Slide 1
Bryce
Canyon
City
Tropic
12
5 Miles
0
N
Bryce Canyon
National Park
Monitoring Vegetation Health and Water Availability in Bryce Canyon National Park for Drought Stress Mitigation Planning
Apply sophisticated remote sensing techniques to:
  Detect springs, seeps, and groundwater-dependent ecosystems
  Understand changes in vegetation presence and health
  Visualize changes in climate
Create a framework for future applications
Objectives
Methodology
Study Area
Results
NDVI and NDWI alone are not a reliable indicator of spring and seep presence
Maximum Entropy models predicted the probability of where springs and seeps are located
Snowfall and snow sublimation have decreased since 1979 while rainfall has remained consistent; pervasive drought conditions suggest that snow is an important contributor to vegetation health
Conclusions
Partners: Tyra Olstad (Bryce Canyon National Park, National Park Service)
Advisors: Sean McCartney (Science Systems & Applications, Inc., GSFC)
Fellows: Carli Merrick (Science Systems & Applications, Inc., GSFC) and Nicole Ramberg-Pihl (Science Systems & Applications, Inc., GSFC)
Special thanks: Dr. Jessica Erlingis (University of Maryland, GSFC)
This model contains modified LIDAR (2018) data from UGRC, NAIP (2021) and Soil Survey data collected by USDA, geological features maps (2022) from USGS and altered by NPS, and PlanetScope Data (2017-2022).
Acknowledgements
Bryce Canyon National Park is home to groundwater-dependent ecosystems (GDEs) that are threatened by a multidecadal drought and increased groundwater extraction due to a spike in tourism. These ecosystems contain unique species that are only found in areas where near-surface groundwater is present, such as aspen groves and fens. These species contribute to the high biodiversity found in Bryce Canyon, which boosts an ecosystem’s productivity and the services it provides to the park. Unfortunately, many of these GDEs are too small to identify with traditional Earth observation platforms and are difficult to physically reach for monitoring purposes. This project partnered with the National Park Service to identify springs and seeps as a proxy for GDEs within Bryce Canyon from 2013–2022. The team mapped groundwater discharge with high resolution National Agriculture Imagery Program (NAIP) and assessed park vegetation trends with Landsat 8 Operational Land Imager (OLI) and PlanetScope imagery. In-situ precipitation data and the Western Land Data Assimilation System (WLDAS) were used to produce time series of climatic variables. Seeps and spring locations were predicted using random forest classification and maximum entropy machine learning models.
Abstract
Node Location
Melanie Frost
Ashley Grinstead
Aaron Carr
Project Lead
Alissa Stark
Team Members
Bryce Canyon Water Resources
Project Partner
Earth Observations
Landsat 8 OLI
PlanetScope DOVEs
Fall 2022
No Date
NAIP Imagery (USDA)
2021
Geologic Formations (USGS)
2022
LiDAR (URGC)
2018
Soil Types (SSURGO)
Maximum Entropy
Spring or Seep Prediction Map
Predictive Modeling
0.90 to 1.00
0.75 to 0.90
0.50 to 0.75
0.00 to 0.50
Predicted Probability of Seep or Spring
0
5 Miles
N
Bryce Canyon
Vegetation Change
Landsat 8, 2013 to 2022
ESRI, HERE, Utah BLM
N
0
5 Miles
Bryce Canyon
Predicted Groundwater
MEM, 2017 to 2022
Input
Analysis
Output
How have they changed over time?
Change Maps
Time Series
Direct Detection
How has vegetation and water changed in space?
Are spring and seep NDVI/NDWI values statistically unique?
Cloud & Shadow Masks, NDVI
PlanetScope DOVEs (PlanetExplorer)
Landsat 8 OLI
(USGS)
2017 – 2022
2013 – 2022
(Google Earth Engine & ArcGIS Pro)
NDVI/NDWI
2018
Input
Analysis
Output
(ArcGIS Pro)
Utah Geospatial Resource Center
Vegetation Trend
(Mann-Kendall Statistic)
Maryland - Goddard
NAIP Imagery
(USDA)
Increasing NDVI
Decreasing NDVI
No Change